## Slide 1: Chapter 1 Introduction

## Slide 2: Outline
A BRIEF HISTORY
PROTOCOLS AND STANDARDS
STANDARDS ORGANIZATIONS
INTERNET STANDARDS
INTERNET ADMINISTRATION

## Slide 3
A
BRIEF
HISTORY
1.1
The McGraw-Hill Companies, Inc., 2000

## Slide 4: Internet
Network
  A group of connected, communicating devices, such as computers and printers
internet
  Two or more network that can communicate with each other
Internet
  The most notable internet
  A collaboration of more than hundreds of thousands interconnected networks

## Slide 5: Time Line
The following is a list of important Internet events in chronological order:
1969. Four-node ARPANET established
  UCLA, UCSB, Stanford Research Institute, and University of Utah
1972. Birth of the Internet by introducing gateways
  Connect different networks that have diverse packet size, interface and transmission rate
1973. Development of TCP/IP suite begins.
1977. An internet, consisting of ARPANET, packet radio, and packet satellite, tested using TCP/IP

## Slide 6: Time Line (Cont.)
1981. UC Berkeley modified the UNIX to include TCP/IP.
1981. CSNET established
  A network sponsored by NSF
1983. TCP/IP becomes the official protocol.
1983. MILNET was born since ARPANET split into
  MILNET: military users, ARPANET: otherwise

## Slide 7: Time Line (Cont.)
1986. NSFNET established
  A backbone (T1 line) that connected five supercomputer centers
1990. ARPANET was replaced by NSFNET
1991, ANSNET established
  A new, high-speed backbone
1995. NSFNET became a research network
1995. ISPs started

## Slide 8
Figure 1-1
Internet Today
The McGraw-Hill Companies, Inc., 2000

## Slide 9
PROTOCOLS
AND
STANDARDS
1.2
The McGraw-Hill Companies, Inc., 2000

## Slide 10: Protocols
Protocol
  A set of rules that governs data communications
Three key elements
  Syntax
    Structure and format of the data (i.e, packets)
  Semantics
    The meaning of each section of bits
  Timing
    When data should be sent
    How fast it can be sent

## Slide 11: Standards
Standards
  Maintain an open market for manufactures
  Guarantee interoperability of data communication
Two categories
  De facto: by fact
    Have not been approved but have been adopted through widespread use
  De jure: by law
    Legislated by an officially body

## Slide 12
STANDARDS
ORGANIZATIONS
1.3
The McGraw-Hill Companies, Inc., 2000

## Slide 13: Standard Organizations
Standard Organizations
  Standard creation committees
  Forums
  Government regulatory agencies

## Slide 14
Standards Creation Committees
International Standards Organization (ISO)
International Telecommunications Union–
Telecommunication Standards Sector (ITU-T)
Institute of Electrical and Electronics Engineers (IEEE)
Electronic Industries Association (EIA)
American National Standards Institute (ANSI)
The McGraw-Hill Companies, Inc., 2000
Word Wide Web Consortium (W3C)
Open Mobile Alliance (OMA)

## Slide 15
Forums
Regulatory Agencies
Frame Relay Forum
ATM Forum
Federal Communications Commission (FCC) in United States
The McGraw-Hill Companies, Inc., 2000
Universal Plug and Play (UPnP) Forum

## Slide 16
INTERNET
STANDARDS
1.4
The McGraw-Hill Companies, Inc., 2000

## Slide 17: Internet Standard
Internet Standard
  A thoroughly tested specification that is useful to and adhered to by those work with the Internets

## Slide 18: Internet Standard (Cont.)
A specification must go through a strict procedures to attain Internet standard status
  First, a specification begins as an Internet draft
  Then, a draft may be published as a Request for Comment (RFC)
  After that, RFC go through maturity levels and are categorized according to there requirement level

## Slide 19: Maturity Level
Proposed standard
  The specification is tested and implemented
Draft standard
  Proposed standard is elevated to draft standard after at least two successful independent and interoperable implementations
Internet standard
  Demonstrations of successful implementation

## Slide 20: Maturity Level (Cont.)
Historic
  Superseded by later specification or failed to become an Internet standard
Experimental
Informational
  Contain general, historical, or tutorial information related to the Internet
  Usually written by non-Internet organization, such as vendor

## Slide 21
Figure 1-2
Maturity levels of an RFC
The McGraw-Hill Companies, Inc., 2000

## Slide 22: Requirement Levels
Required
  Must be implemented by all Internet systems
  For example, IP and ICMP
Recommended
  Not for conformance but for usefulness
  For example, FTP and TELNET
Elective
  A system can use elective for its own benefit

## Slide 23: Requirement Levels (Cont.)
Limited use
  Most of the experimental RFCs fall under this category
  Used only in limited situations
Not recommended
  A historic RFC may fall under this category

## Slide 24
Figure 1-3
Requirement Levels of an RFC
The McGraw-Hill Companies, Inc., 2000

## Slide 25
RFCs can be found at http://www.rfc-editor.org.
Note

## Slide 26
INTERNET
ADMINISTRATION
1.5

## Slide 27
Internet Administration
Internet Society (ISOC)
Internet Architecture Board (IAB)
Internet Engineering Task Force (IETF)
Internet Research Task Force (IRTF)
Internet Assigned Numbers Authority (IANA) and Internet Corporation for Assigned Names and Numbers (ICANN)
Network Information Center (NIC)