## Slide 1: Chapter 10 Mobile IP

## Slide 2: Outline
Addressing
Agents
Three Phases
Inefficiency in Mobile IP

## Slide 3: Addressing
Addressing
  The main problem that must be solved in mobile communication using the IP protocol
The original IP address was based on the assumption that a host is stationary
  Routers use the hierarchical structure of an IP address to route an IP datagram
  The address is valid only when it is attached to the network
    If the network changes, the address is no longer valid

## Slide 4
The IP addresses are designed to work with stationary hosts because part of the address defines the network to which the host is attached.
Note

## Slide 5: Mobile Hosts
When a host moves from one network to another
  The IP addressing structure needs to be modified
Possible solutions
  Changing the address
  Two addresses

## Slide 6: Changing the Address
The mobile host changes its address as it goes to the new network
  For example, DHCP protocol
Drawbacks
  The configuration files would need to be changed
  Each time the computer moves from one network to another, it must be rebooted
  The DNS tables need to be revised so that every other host in the Internet is aware of the change
  If the host roams from one network to another during a transmission, the data exchange will be interrupted
    Since the port and IP addresses of the client and the server must remain constant for the duration of the connection

## Slide 7: Two Addresses
The host has
  Its original address, called the home address
    Permanent and associate the host to its home network
  A temporary address, called the care-of address
    Temporary
    When a host moves from one network to another, the care-of address changes
    Associate the host with the foreign network
    A mobile host receives its care-of address during the agent discovery and registration phases

## Slide 8
Figure 27-1
Host Address and Care-of Address
The McGraw-Hill Companies, Inc., 2000

## Slide 9
Mobile IP has two addresses for a mobile host: one home address and one care-of address. The home address is permanent; the care-of address changes as the
mobile host moves from one network to another.
Note

## Slide 10: Outline
Addressing
Agents
Three Phases
Inefficiency in Mobile IP

## Slide 11: Agents
To support Mobile IP, there are two agents
  Home agent and foreign agent
Home agent
  Usually a router attached to the home network of the mobile host
  Acts on behalf of the mobile host when a remote host sends a packet to the mobile host
    The home agent then sends it to the foreign agent

## Slide 12: Agents
Foreign Agent
  Usually a router attached to the foreign network
  Receive and delivers packets sent by the home agent to the mobile host
A mobile host can also act as a foreign agent
  The care-of address is called a colocated care-of address
  Advantages:
    The mobile host can move to any network without worrying about the availability of a foreign agent
  Disadvantages
    The mobile host needs extra software to act as its own foreign agent

## Slide 13
Figure 27-2
Home Agent and Foreign Agent
The McGraw-Hill Companies, Inc., 2000

## Slide 14: Outline
Addressing
Agents
Three Phases
Inefficiency in Mobile IP

## Slide 15: Three Phases
To communicate with a remote host, a mobile host goes through three phases
  Agent discovery
    Involve the mobile host, the foreign agent, and the home agent
  Registration
    Involve the mobile host and two agents
  Data transfer
    All four entities are involved

## Slide 16
Figure 27-3
Remote Host and Mobile Host Communication
The McGraw-Hill Companies, Inc., 2000

## Slide 18: Agent Discovery
Consist of two subphases
  A mobile host must discover a home agent before it leaves its home network
  A mobile host must also discover a foreign agent after it has moved to a foreign network
The discovery involves two types of messages
  Advertisement and solicitation

## Slide 19: Agent Advertisement
When a router advertises its presence on a network using an ICMP router advertisement
  It can append an agent advertisement to the packet if it acts as an agent

## Slide 20: Packet Format of Agent Advertisement
Type: set to 16
Length:8-bit
  Define the total length of the extension message
Sequence Number: 16-bit
  Hold the message number
Lifttime: 16-bit
  Define the number of seconds that the agent will accept the request
Code: 8-bit
  See the Table 27.1
Care-of-Address: a list of addresses available for uses as care of address. This field is used only by a foreign agent
  The mobile host can choose one of these addresses.
  The selection of this care-of address is announced in the registration request message

## Slide 21
Figure 27-4
Agent Advertisement
The McGraw-Hill Companies, Inc., 2000

## Slide 22: Code Bits

## Slide 23: Agent Solicitation
When a mobile host has moved to a new network and has not received agent advertisements
  It can initiate an agent solicitation

## Slide 24: Registration
After a mobile host has moved to a foreign network and discovered the foreign agent, it must register

## Slide 25: Registration Request and Reply
Registration request and registration reply
  To register with the foreign agent and the home agent

## Slide 26: Registration Request
Sent from the mobile host to the foreign agent
  To register its care-of address
  To announce its home address and home agent address
The foreign will then relay the request to the home agent
  Home agent now knows the address of the foreign agent
    Since the relay packet’s source address is the foreign agent’s IP address

## Slide 27: Registration Request Format
Type: 8-bit
  Define the type of the message
Flag: 8-bit
  Define forwarding information.
  The value of each bit can be set or unset. See next two slide
Lifetime: 16-bit
  Define the number of seconds the registration is valid
  If a string of 0s: the request message is deregistration
  If a string of 1s: the lifetime is infinite

## Slide 28
Registration Request Format
The McGraw-Hill Companies, Inc., 2000

## Slide 29: Registration Request Flag Field Bits

## Slide 30: Registration Request Format (Cont.)
Home address: 32-bit
  Contain the permanent address of the mobile host
Home agent address: 32-bit
  Contain the address of the home agent
Care-of address: 32-bit
  Contain the temporary address of the mobile host
Identification: 64-bit
  Inserted into the request by the mobile host and repeated in the reply message
  Used to match a request with a reply
Extension:
  Variable length extensions are used for authentication

## Slide 31: Registration Reply
Sent from the home agent to the foreign agent and then relayed to the mobile host
Used to confirms or denies the registration request
Format: similar to those of the registration request
  Code field replaces the flag field
    Show the result of the registration request (acceptance or denial)

## Slide 32
Figure 27-7
Registration Reply Format
The McGraw-Hill Companies, Inc., 2000

## Slide 33: Encapsulation
Registration message are encapsulated in a UDP user datagram

## Slide 34: Data Transfer
After agent discovery and registration, a mobile host can communicate with a remote host
  From remote host to home agent
  From home agent to foreign agent
  From foreign agent to mobile host
  From mobile host to remote host

## Slide 35
Figure 27-8
Data Transfer
The McGraw-Hill Companies, Inc., 2000

## Slide 36: From Remote Host to Home Agent
A remote host sends a packet to a mobile host
  Source address: the address of the remote host
  Destination address: the home address of the mobile host
The packet is intercepted by the home agent, which pretends it is the mobile host
  Using the proxy ARP discussed in Chapter 7

## Slide 37: From Home Agent to Foreign Agent
After receiving the packet, the home agent sends the packet to the foreign agent
  Using the tunneling concept
  The home agent encapsulates the whole IP packet inside another IP packet
    Source address: the home agent’s address
    Destination address: the foreign agent’s address

## Slide 38: From Foreign Agent to Mobile Host
When the foreign agent receives the packet
  It removes the packet header added by tunneling
  Then change the home address of the mobile host to its care-of address
  Then send the packet to the mobile host

## Slide 39: From Mobile Host to Remote Host
When a mobile host wants to send a packet to a remote host
  It sends as it does normally
  Source address: the mobile host’s home address
  Destination address: the remote host’s address

## Slide 40: Transparency
The remote host is unaware of any movement by the mobile host
  To send packet
    Destination address: the home address of the mobile host
  To receive packet
    Source address: the home address of the mobile host
Thus, the movement is totally transparent

## Slide 41: Outline
Addressing
Agents
Three Phases
Inefficiency in Mobile IP

## Slide 42: Inefficiency in Mobile IP
Communication involving mobile IP can be inefficient
  Double crossing: or 2X
  Triangle routing: dog-leg routing

## Slide 43: Double Crossing
Occurs when a remote host communicates with a mobile host that has moved to the same network as the remote host
When the mobile host sends a packet to the remote host
  There is no efficiency; the communication is local
When the remote host sends a packet to the mobile host
  The packet crosses the Internet twice

## Slide 44
Figure 27-9
Double Crossing
The McGraw-Hill Companies, Inc., 2000

## Slide 45: Triangle Routing
Occurs when the remote host communicates with a mobile host that is not attached to the same network as the remote host
When the mobile host sends a packet to the remote host
  There is no efficiency
When the remote host sends a packet to the mobile host
  The packet goes from the remote host to the home agent and then to the mobile host
  The packet travels the two sides of a triangle

## Slide 46
Figure 27-10
Triangle Routing
The McGraw-Hill Companies, Inc., 2000

## Slide 47: Solution
The remote host must know the mobile host’s care-of address
  Send packet using the mobile host’s care-of address
  The home agent can tell the remote host about this information by the update binding packet
However, when the mobile host moves, its care-of address may be changed
  The home agent needs to send a warning packet to the remote host to inform it