## Slide 1: Chapter 11 Unicast Routing Protocols: RIP, OSPF, and BGP

## Slide 2: Outline
Introduction
Intra- and Inter-Domain Routing
Distance Vector Routing
RIP
Link State Routing
OSPF
Path Vector Routing
BGP

## Slide 3: Introduction
An internet is a combination of networks connected by routers
How to pass a packet from source to destination ?
  Which of the available pathways is the optimum pathway ?
Depends on the metric
  Metric: a cost assigned for passing through a network
  A router should choose the route with the smallest metric

## Slide 4: Introduction (Cont.)
The metric assigned to each network depends on the type of protocol
  RIP (Routing Information Protocol)
    Treat each network as equal
    The cost of passing through each network is the same: one hop count
  Open Shortest Path First (OSPF)
    Allow administrator to assign a cost for passing through a network based on the type of service required
      For example, maximum throughput or minimum delay
  Border Gateway Protocol (BGP)
    The criterion is the policy, which can be set by the administrator

## Slide 5: Introduction (Cont.)
Routing table can be static or dynamic
  An internet needs dynamic routing tables
Dynamic routing table is achieved by the routing protocols

## Slide 6: Outline
Introduction
Intra- and Inter-Domain Routing
Distance Vector Routing
RIP
Link State Routing
OSPF
Path Vector Routing
BGP

## Slide 7: Interior and Exterior Routing
An Internet can be so large
  One routing protocol cannot handle the task of updating routing table of all routers
Thus, an Internet is divided into autonomous systems (AS)
  AS is a group of networks and routers under the authority of a single administration

## Slide 8: Intra- And Interdomain Routing
intradomain routing
  Routing inside an autonomous system
  Each AS can chose its own intradomain routing protocol
  Examples: distance vector and link state
interdomain routing
  Routing between autonomous systems
  Only one interdomain routing protocol is usually used between ASs
  Examples: path vector

## Slide 9: Example: Autonomous Systems

## Slide 10: Intradomain Routing Algorithms
Distance-vector routing algorithm
  Classical Distributed Bellman-Ford algorithm
  RIP (Routing Information Protocol)
Link-state routing algorithm
  Centralized version of the shortest path computation
    Every router has the whole “picture” of the internet
  OSPF (Open Shortest Path First)

## Slide 11
Figure 13-1
Popular Routing Protocols
The McGraw-Hill Companies, Inc., 2000

## Slide 12: Outline
Introduction
Intra- and Inter-Domain Routing
Distance Vector Routing
RIP
Link State Routing
OSPF
Path Vector Routing
BGP

## Slide 13: Distance Vector Routing
The least cost route between any two nodes is the route with minimum distance.
Each node maintains a vector (table) of minimum distances to every node

## Slide 14: Distance Vector Routing Tables

## Slide 15: Initialization
At the beginning
  Each node can know only the distance between itself and its immediate neighbors
  We assume each node can send a message to the immediate neighbors and find the distance

## Slide 16: Initialization of Tables in Distance Vector Routing

## Slide 17: Sharing
Idea of distance vector routing
  Sharing of information between neighbors
  In distance vector routing, each node shares its routing table with its immediate neighbors periodically and when there is a change
How much of the table must be shared ?
  Send the entire table but contains only the first two columns
    The third column must be changed

## Slide 18: Updating
Receipt: a two-column table from a neighbor
Add the cost between itself and the sending node to each value in the second column
Repeat the following steps for each advertised destination
  If (destination not in the routing table)
    Add the advertised information to the table
  Else
    If (next-hop field is the same)
      Replace retry in the table with the new advertised one
    Else
      If (advertised hop count smaller than one in the table)
        Replace entry in the routing table

## Slide 19: Updating in Distance Vector Routing
Reach A via C

## Slide 20: When to Share
The table is sent both periodically and when there is a change in the table
Periodic update
  A node sends its routing table in a periodic update
  Normally every 30 seconds
Triggered update
  A node receives a table from a neighbor resulting in changes in its own table
  A node detects some failure in the neighboring links which results in a distance change to infinity

## Slide 21: Count to Infinity
A problem with distance vector routing is count to infinity
  If a link is broken (cost becomes infinity), every other router should be aware of it immediately
  But, in distance vector routing, this takes some time
As a result, distance vector routing has the problem of instability
  A network using this protocol can become unstable
  Caused by a link has been broken, but routers has not yet known

## Slide 22: Two-Node Loop Instability
One example of count to infinity is the two-node loop problem.
See the following table
  1. both node A and B know how to reach node X
  2. the link between A and X fails
    Node A change its table
  3a. If node A can send its routing table to B immediately
    Everything is fine
  3b. However, if node B sends its routing table to A first
    Node A assumes that B has found a way to reach X
  4. A sends its new update to B and B also update its routing table
  5. B sends its new update to A and so on…until the cost reach infinity
  6. Then both A and B knows that the link is broken

## Slide 23: Two-Node Instability
1

## Slide 24: Two-Node Loop Instability (Cont.)
As a result, during the time before cost reaches infinity
  A packet destined for X bounces between A and B
  Create a two-node loop instability
Solutions
  Defining infinity
  Split horizon
  Split horizon and poison reverse

## Slide 25: Defining Infinity
Redefine infinity to a smaller number
  Shorten the time of instability
Most implementation define the distance between each node to be 1
  Define 16 as infinity
As a result
  The distance vector scheme cannot be used in large system
  The size of network, in each direction, can not exceed 15 hops

## Slide 26: Split Horizon
Do not flood the table through each interface and a router must distinguish between different interface
If a router received route updating message from an interface
  This same updated information must not be sent back through this interface
  Since the information has come from the sending one

## Slide 27
Split Horizon
The McGraw-Hill Companies, Inc., 2000
B receives information about Net1 and Net2 through its left interface
This information is updated and passed on through the right interface but not to the left

## Slide 28: Split Horizon (Cont.)
Thus, in the figure of two-node instability
  Node B eliminates the last line of its routing table before it sends to A
    Node A then keeps the value of infinity as the distance to X
  Later when A sends its routing table to B
    B then correct its routing table
The system becomes stable after the first update
  Both node A and B know that X is not reachable

## Slide 29: Split Horizon and Poison Reverse
Drawback of split horizon
  Distance vector uses a timer
    If there is no news about a route within the time duration
    Delete the route
  Since Node B eliminates the route to X
    Node A cannot decide it is due to split horizon or because B has not received any news about X recently
Solution: Split Horizon and Poison Reverse

## Slide 30: Split Horizon and Poison Reverse
A variation of split horizons
Information received is used to update routing table and then passed out to all interface
However, a table entry is set to a metric of infinity as it’s come through and goes out interface are the same
For example
  Router B has received information about Net1 and Net2 through its left interface
  Thus, it sends information out about Net1 and Net2 with a metric of 16 to its left interface (assume 16 is infinity)

## Slide 31
Split Horizon and Poison Reverse
The McGraw-Hill Companies, Inc., 2000

## Slide 32: Three-Node Instability
Split Horizon and Poison Reverse cannot solve three-node instability
1. A detects X is not reachable
    Sends a packet to B and C
2. B updates its table but the packet to C is lost
3. After a while, C sends to B its routing table
    B is fooled and updates its routing table
5. B sends its routing table to A
    A is fooled and updates its routing table
6. A then sends its routing table to C, then C to B, and B to A, and so…..
7. The loop continues until the cost reach infinity

## Slide 33: Three-Node Instability

## Slide 34: Outline
Introduction
Intra- and Inter-Domain Routing
Distance Vector Routing
RIP (Skip!)
Link State Routing
OSPF
Path Vector Routing
BGP

## Slide 35: Concept of Link State Routing

## Slide 36: Link State Routing
From above Figure
  Each node uses the same topology to create a routing table
  But the routing table for each node is unique
    Like a city map

## Slide 37: Link State Routing
Assumption of link state routing
  Although the global topology knowledge is not clear and each node has partial knowledge
    It knows the state (type, condition, cost) of its link
  However, the whole topology can be compiled from the partial knowledge of each node
    See the next Figure

## Slide 38
Link State Knowledge
Each node has a partial knowledge of the network
There is an overlap in the knowledge
The overlap guarantees the creation of a common topology
  A picture of the whole domain for each node

## Slide 39: Building Routing Tables
Four sets of actions in link state routing
  Creation of the states of the links by each node
    Called the link state packet or LSP
  Dissemination of LSPs to every other router, called flooding, in an efficient and reliable way
  Formation of a shorten path tree for each node
  Calculation of a routing table based on the shortest path tree

## Slide 40: Creation of Link State Packet (LSP)
Assume a LSP carries
  The node identity
  The list of links
    Both are needed to make the topology
  A sequence number
    Distinguishes new LSPs from old ones
  Age
    Prevent old LSPs from remaining in the domain for a long time

## Slide 41: Creation of Link State Packet (LSP)
LSP are generated on two occasions
  When there is a change in the topology of the domain
    Quickly inform any node to update its topology
  On a periodic basis
    The period is much longer compared to the distance vector routing
    60 minutes or 2 hours

## Slide 42: Flooding of LSPs
Flooding: the LSP must be disseminated to all other nodes in the domain
  Not only to its neighbors
Rules
  The creating node sends a copy of the LSP out of each interface
  All receiving nodes compare the incoming one with the copy it may already have
    If the newly LSP is older than the one it has by checking sequence number
      Discard the LSP
    Else
      Discard the old LSP
      Sends a copy of it out of each interface except the incoming one

## Slide 43: Formation of Shortest Path Tree: Dijkstra Algorithm

## Slide 44
Figure 14.18 Example of formation of shortest path tree

## Slide 45: Calculation of Routing Table from Shortest Path Tree
Example:

## Slide 46: Outline
Introduction
Intra- and Inter-Domain Routing
Distance Vector Routing
RIP
Link State Routing
OSPF (Skip!)
Path Vector Routing
BGP

## Slide 47: Areas
OSPF divides an autonomous system into areas
  To handle routing efficiently and in a timely manner
A collection of networks, hosts, and routers all contained within an autonomous system
Thus, an autonomous system can be divided into many different areas
All networks inside an area must be connected

## Slide 48: Areas (Cont.)
Routers inside an area flood the area with routing information
At the border of an area, special routers called area border routers
  Summarize the information about the area and sent it to other areas

## Slide 49: Areas (Cont.)
Among the area inside an autonomous system is a special area called backbone
  All of the areas inside an AS must be connected to the backbone
The routers inside the backbone are called the backbone routers
  A backbone router can also be an area border router

## Slide 50: Areas (Cont.)
If the connectivity between a backbone and an area is broken
  A virtual link must be created by the administration
Each area has an area identification
  The area identification of the backbone is zero

## Slide 51
Areas in an Autonomous System
The McGraw-Hill Companies, Inc., 2000

## Slide 52: Metrics
OSPF allows the administrator to assign a cost, called the metric, to each route
Metric can be based on a type of service
  Minimum delay
  Maximum throughput
A router can have multiple routing tables
  Each based on a different type of service

## Slide 53: Types of Links
In OSPF, a connection is called a link
Four types of links
  Point-to-point
  Transient
  Stub
  Virtual

## Slide 54
Types of Links
The McGraw-Hill Companies, Inc., 2000

## Slide 55: Point-to-Point Link
Connect two routers without any other host or router in these two routers
Example
  Telephone line
  T-line
Graphically representation
  The routers are represented by nodes
  The link is represented by a bidirectional edge
The metric
  Usually the same at the two ends

## Slide 56
Point-to-Point Link
The McGraw-Hill Companies, Inc., 2000

## Slide 57: Transient Link
A network with several routers attached to it
  Data can enter through any of the routers and leave through any router
Example
  All LANs and some WANs with two or more routers

## Slide 58: Transient Link (Cont.)
Graphically representation
  Figure b in the next slide. However, it is
    Not efficient: each router need to advertise the neighborhood of four other routers
      For a total of 20 advertisement
    Not realistic: there is no single network (link) between each pair of routers
      There should be only one network that serves as a crossroad between all five routers

## Slide 59: Transient Link (Cont.)
Reality: each router should be connected to every router through one single network
  The network is represented by a node
  However, network is not a machine
    Cannot function as a router
Solution: one of the routers acts as a single network
  This router has a dual purpose: a true router and a designated router
    The link is represented as a bidirectional edge
    Figure c in the next slide

## Slide 60
Transient Link
The McGraw-Hill Companies, Inc., 2000

## Slide 61: Stub Link
A network that is connected to only one router
  Data packet enter and leave through this only one router
A special case of transient network
Graphically representation
  The router as a node
  The designated router as the network
  Note, the link is only one-directional
    From the router to the network
    Because the network is the end point in the graph representation
      See the following third slides

## Slide 62
Stub Link
The McGraw-Hill Companies, Inc., 2000

## Slide 63: Virtual Link
When the link between two routers is broken
  The administrator may create a virtual path between them using a longer path and may go through several routers

## Slide 64
Example of an AS and its graphical representation in OSPF

## Slide 65: Types of Packets
OSPF uses five different packets
  Hello packet
  Database description packet
  Link state request packet
  Link state update packet
    Router link
    Network link
    Summary link to network
    Summary link to AS boundary router
    External link
  Link state acknowledgment packet

## Slide 66
Figure 13-33
Types of OSPF Packets
The McGraw-Hill Companies, Inc., 2000

## Slide 67: Router Link LSA
Define the link of a true router
A true router uses this advertisement to announce information about
  All of its links
  What is at the other side of the links (neighbors)

## Slide 68
Router Link

## Slide 69: Network Link LSA
Define the links of a network
A designated router, on behalf of the transient network, distributes this type of LSA packet
Announce the existence of all of the routers connected to the network
  See Next Fig.

## Slide 70
Network Link

## Slide 71: Summary Link to Network LSA
Router link and network link advertisements
  Flood the area with information inside an area
But a router must also know about the networks outside its area
  The area border routers provide this information
An area border router is active in more than one area
  Receive router link and network link advertisements
  Create a router table for each area
  Provide one area’s information to other areas by the summary link to network advertisement

## Slide 72: Example
R1 is an area border router and has two routing tables
  One for area 1 and one for area 0
R1 will flood area 1 with information about how to reach a network located in area 0
R2 plays the same role

## Slide 73
Summary Link to Network

## Slide 74: Summary Link to AS Boundary Router LSA
Previous advertisement lets every router know the cost to reach all of the networks inside the AS
But, how to reach a network outside an AS?
A router must know how to reach the autonomous boundary router first
The summary link to AS boundary router provides this information
  The area border routers flood their area with this information

## Slide 75
Figure 13-29
Summary Link to AS Boundary Router LSA
The McGraw-Hill Companies, Inc., 2000

## Slide 76: Summary Link to AS Boundary Router LSA (Cont.)
Announce the route to an AS boundary router
  Define the network to which the AS boundary router is attached
  The area border routers flood their area with this LAS

## Slide 77
Figure 14.41 Summary link to AS boundary router LSA

## Slide 78: External Link LSA
How a router inside an AS know which networks are available outside the AS ?
  The external link advertisement provides this information
The AS boundary routers floods the autonomous system with the cost of each network outside the AS
  Using a routing table created by an exterior routing protocol
Notably, each advertisement announces one single network
  Separate announcements are made if more than one network exists Announce all the networks outside the AS

## Slide 79: External Link LSA (Cont.)
Use to announce all of the networks outside the AS

## Slide 80: Encapsulation
OSPF packets are encapsulated in IP datagram
  OSPF contains the acknowledgment mechanism for flow and error control
  Doe not need a transport layer protocol to provide these services

## Slide 81: Outline
Introduction
Intra- and Inter-Domain Routing
Distance Vector Routing
RIP
Link State Routing
OSPF
Path Vector Routing
BGP

## Slide 82: Path Vector Routing
Why distance vector routing and link state routing are not good candidates for interdomain routing?
Mostly because of scalability
  Intractable when the domain of operation becomes large

## Slide 83: Path Vector Routing (Cont.)
Distance vector routing
  Unstable if there is more than a few hops in the domain
Link state routing
  An Internet is usually too big for this routing method
    Need a huge amount of resources to calculate routing table
    Create heavy traffic because of flooding
Solution
  Path vector routing

## Slide 84: Path Vector Routing (Cont.)
There is one node in each AS to act on behalf of the entire AS
  Called it speaker node
The speaker node in an AS
  Creates a routing table
  Advertises the routing table to speaker nodes in the neighboring ASs
  Furthermore, a speaker node advertises the path
    Not the metric of the nodes

## Slide 85: Initialization
At the beginning, each speaker node can know only the reachability of nodes inside its AS
Example
  See the Following 14.48

## Slide 86
Figure 14.48 Initial routing tables in path vector routing

## Slide 87: Sharing
A speaker in an AS share its table with immediate neighbors
Example
  In Fig. 14.48
  A1 share with B1 and C1

## Slide 88: Updating
When a speaker node receives a two-column tables, update its table
  Add the nodes that are not in its routing table
  Add its own AS and AS that sent the table
Example
  Fig. 14.49 shows a stabilized table
  If A1 receives a packet for node A3
    The path is in AS1 (the packet is at home)
  If D1 receives a packet for node A2
    The packet should go from AS4 to AS3, and then to AS1

## Slide 89
Figure 14.49 Stabilized tables for four autonomous systems

## Slide 90: Loop Prevention
Path vector routing can avoid the instability of distance vector routing and the creation of loops
When a router receives a table sent from other node
  Check if its AS is in the path list
  If yes, looping is involved => ignore the table

## Slide 91: Policy Routing
Policy routing can be easily implemented through path vector routing
  Path vector routing lists all the ASs of each path
  Once a router receives a message, it can check the path.
  If one of the AS listed in the path is against its policy,
    It can ignore that path and that destination
      Does not update its routing table with this path
      Does not send this message to its neighbors
Thus, path vector routing are not based on the smallest hop count or the minimum metric
  Based on the policy imposed on the router by the administrator

## Slide 92: Optimum Path
The optimum path is the path that fits the organization
  Criteria may be: hop count, security and safety, reliability
Path vector routing can achieve optimum path by looking for a path best for the organization
  Since all the AS are listed in the path

## Slide 93: Outline
Introduction
Intra- and Inter-Domain Routing
Distance Vector Routing
RIP
Link State Routing
OSPF
Path Vector Routing
BGP (Skip!)