## Slide 1: Chapter 13 Introduction to the Transport Layer

## Slide 2
Figure 8-1
Position of IP in TCP/IP Protocol Suite
The McGraw-Hill Companies, Inc., 2000

## Slide 3: Outline
Transport-layer services
Transport-layer protocols

## Slide 4: Transport-Layer Services
Process-to-process communication
Addressing: Port Numbers
Encapsulation and Decapsulation
Multiplexing and Demultiplexing
Flow Control
Error Control
Combination of Flow and Error Control
Congestion Control
Connectionless and Connection-Oriented Services

## Slide 5: Process-to-Process Communication
Network layer: host-to-host communication
  Deliver the message to the destination computer
Transport layer: process-to-process communication
  Deliver the message to the appropriate process

## Slide 6: Addressing: Port Numbers
To achieve process-to-process communication: client-server paradigm
Example:
  Ftp client and ftp server
  WWW server and WWW client (browser)
  …..

## Slide 7: Addressing: Port Numbers (Cont.)
Port numbers: define the processes
0~65535
Well-known port numbers
  Servers needs to be assign a universal port number
  So that client process knows the port number of the server process
However, client’s port number can be defined randomly
  Ephemeral (=short lived) port number

## Slide 8
Figure 11-3
Port Numbers
The McGraw-Hill Companies, Inc., 2000

## Slide 9
Figure 11-4
IP Addresses Versus Port Numbers
The McGraw-Hill Companies, Inc., 2000

## Slide 10: IANA Ranges
The IANA divides the port numbers into three ranges
  Well-known ports: assigned and controlled by IANA
    0~1,023
  Registered ports: not assigned or controlled by IANA
    1,024~49,151
    Can only be registered with IANA to prevent duplication
  Dynamic (or private) ports: neither controlled nor registered
    49152~65535
    Ephemeral ports and can by used by any process

## Slide 11
In UNIX, the well-known ports are stored in a file called /etc/services. Each line in this file gives the name of the server and the well-known port number. We can use the grep utility to extract the line corresponding to the desired application. The following shows the port for TFTP. Note that TFTP can use port 69 on either UDP or TCP. SNMP (see Chapter 24) uses two port numbers (161 and 162), each for a different purpose.
Example 13.1

## Slide 12: Socket Addresses
Transport layer protocol needs two identifiers at each end
  The IP addresses
  The port numbers
Socket address
  The combination of an IP address and a port number
  Thus, we need a pair of socket addresses for a transport layer communication
    Client socket address and server socket address

## Slide 13
Figure 11-6
Socket Addresses
The McGraw-Hill Companies, Inc., 2000

## Slide 14: Encapsulation and Decapsulation in the Transport Layer

## Slide 15: Multiplexing and Demultiplexing
Multiplexing (many to one)
  Performed at the source
  Accepts item from more than one source
Demultiplexing (one to many)
  Performed at the destination
  Deliver item to more than one source

## Slide 16: Multiplexing and Demultiplexing

## Slide 17: Flow Control
There should be a balance between producer and consumer
  If the items are produced faster than are consumed
    The consumer can be overwhelmed and discard items
  If the items are produced slower than are consumed
    The consumer should wait and system is less efficient
Flow control:
  Related to the first issue
  Prevent losing the packets at the consumer site

## Slide 18: Pushing or Pulling
Delivery of items from a producer has two ways
  Pushing:
    Deliver items without the prior request from the consumer
    The consumer may be overwhelmed
    Need flow control
  Pulling
    Deliver items after the consumer has requested them
    No need for flow control

## Slide 19: Flow Control at the Transport Layer
As shown in next slide, at least two cases of flow control
  From the sending transport layer to the sending application layer
  From the receiving transport layer to the sending transport layer
The receiving application layer to the receiver transport layer is a pulling delivery
  The transport layer waits until the application-layer process asks for message

## Slide 20: Flow Control at the Transport Layer (Cont.)

## Slide 21: Buffers
One solution to flow control is using two buffers
  One at the sending transport layer and the other at the receiving transport layer
  In the buffer in the sending transport layer
    If it is full: inform the application to stop passing message
    If it has vacancies, inform application to pass message
  In the buffer in the receiving transport layer
    If it is full: inform the sending transport layer to stop sending
    If it has vacancies, inform the sending transport layer to send message

## Slide 22: Error Control
Error control at the transport layer
  Detect and discard corrupted packets
  Keep track of lost and discarded packets and resend them
  Recognize duplicated packets and discard them
  Buffer out-of-order packets until the missing packet arrives
Packets
Error Control

## Slide 23: Sequence Number
To know which packet is lost, duplicated, or out-of-order
  Each packet must be numbered
Solution: sequence number
Note that, sequence number can wrap around
  Example: if sequence number is 4 bits, then
0, 1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 14, 15, 0, 1, 2, 3, 4, 5, 6, …..

## Slide 24: Acknowledgment
Acknowledgment
  Positive acknowledgment
    Send an acknowledgement for packets that have arrived safe and sound
  Negative acknowledgment
    Send an acknowledgement for packets that are not arrived or corrupted

## Slide 25: Combination of Flow and Error Control (Skip!)
Flow control: needs two buffers
Error control: define sequence number and acknowledgement number
Combination of flow and error control
  Two numbered buffers with the sliding window mechanism

## Slide 26: Combination of Flow and Error Control (Skip!)
Example: as shown in the following slide
  The buffer is numbered
  Assume that the sequence number is 4 bits
    Thus, the buffer is numbered from 0 to 15
  Assume that the size of window is 7
However, most protocols show the sliding window using linear representation
  Shown in the next following slide

## Slide 27: Sliding Window in Circular Format (Skip!)

## Slide 28: Sliding Window in Linear Format (Skip!)

## Slide 29: Congestion Control
Congestion
  The load on the network is greater than the capacity of the network
Why?
  An internet is a combination of networks and connecting devices, e.g., routers and switches
  A router/switch has queues that store the incoming packets, processes them, and forward them.

## Slide 30: Congestion Control (Cont.)
In the following features,
  Input queue may be congested
    Packet arrival rate > packet processing rate
  Output queue may be congested
    Packet departure rate < packet processing rate

## Slide 31
Figure 12-14
Router Queue
The McGraw-Hill Companies, Inc., 2000

## Slide 32: Congestion Control Mechanism
Congestion control
  Prevent congestion before it happens
  Remove congestion after it happens
Two categories
  Open-loop congestion control (prevention)
  Closed-loop congestion control (removal)

## Slide 33: Open-Loop Congestion Control
Prevent congestion before it happens
Possible policies
  Retransmission policy
    Retransmission policy and retransmission timer should be designed to optimize efficiency
  Acknowledgment policy
    Does not ACK every packet it receives
  Discard policy
    Router should adopt good discard policy

## Slide 34: Closed-Loop Congestion Control
Try to alleviate congestion after it happens
Possible mechanisms
  Back pressure
    When a router is congested, it can inform the previous upstream router to reduce it outgoing rate
    The action can be recursive all the way to the router just prior to the source
  Choke Point
    A router sends a packet to the source to inform congestion
    This packet is called chock point, like ICMP’s source quench packet
  Implicit signaling
    Source can detect an implicit signal warning of congestion
      For example, the delay in receiving an acknowledgment
  Explicit signaling
    Router can send an explicit signal to the sender or receiver of congestion
      For example, set a bit in a packet

## Slide 35: Connectionless and Connection-Oriented Services
Transport-layer protocol, like network-layer protocol can provide two types of services
  Connectionless and connection-oriented
  However, they have different meaning
Network-layer protocol
  Connectionless service:
    Mean different paths for different datagrams belonging to the same message
  Connection-oriented service
    In contrast

## Slide 36: Connectionless and Connection-Oriented Services (Cont.)
Transport-layer protocol: does not concern with the physical paths of packets
  Connectionless service:
    Mean independency between packets
  Connection-oriented service
    Mean dependency between packets

## Slide 37: Connectionless Services
Each packet is independent
  Even coming from the same source process
Thus, packet may
  be arrived out-of-order, lost, or duplicate
No flow control, error control, and congestion control can be effectively implemented in a connectionless service

## Slide 38: Connectionless Service

## Slide 39: Connection-Oriented Services
In the network layer
  Needs a coordination between the two end hosts and all the routers in between
In transport layer
  Only involves the two ends; the service is end-to-end
  Thus, a connection-oriented transport-layer protocol can be made over either a connectionless or connection-oriented network-layer protocol

## Slide 40: Connection-Oriented Services (Cont.)
As shown in the next slide, need three phase
  Connection establishment
  Data transfer
  Tear-down phases
Flow control, error control, and congestion control can be effectively implemented in a connection-oriented service

## Slide 42: Outline
Transport-layer services
Transport-layer protocols (Skip!)