## Slide 1: Chapter 15 Transmission Control Protocol (TCP)

## Slide 2: Outline
TCP Services
TCP Features
Segment
A TCP Connection
State Transition Diagram
Windows in TCP
Flow Control
Error Control
Congestion Control
TCP Timers
Options
TCP Package

## Slide 3
Figure 12-1
Position of TCP in TCP/IP Protocol Suite
The McGraw-Hill Companies, Inc., 2000

## Slide 4
12.1 TCP SERVICES
We explain the services offered by TCP to the processes at the application layer.
The topics discussed in this section include:
Process-to-Process Communication
Stream Delivery Service
Full-Duplex Communication
Multiplexing and Demultiplexing
Connection-Oriented Service
Reliable Service

## Slide 5: TCP Services
TCP provides services to the processes at the application layer
  Process-to-Process Communication
  Stream Delivery Service
  Full-Duplex Service
  Multiplexing and Demultiplexing
  Connection-Oriented Service
  Reliable Service

## Slide 6: Process-to-Process Communication
Like UDP, TCP provides process-to-process communication using port numbers

## Slide 7: Stream Delivery Service
UDP treats each chunk independently
  No any relationship between the user datagrams
In contrast, TCP allow the data be delivered and received as a stream of bytes

## Slide 8: Stream Delivery Service (Cont.)
However, the sending and receiving speed may not be the same
  TCP needs buffers for storage
Two buffers in TCP
  Sending buffer and receiving buffer, one for each connection
  Also used in flow- and error-control mechanisms

## Slide 9
Figure 12-5
Sending and Receiving Buffers
The McGraw-Hill Companies, Inc., 2000

## Slide 10: Sending Buffers
The sending circular buffer has three types of sections
  White section: empty location
    Can be filled by the sending process
  Color section: hold bytes that have been sent but not yet acknowledged
    TCP keeps these bytes until it receives acknowledges
  Gray section: bytes to be sent by the sending TCP
    TCP may be able to send only part of this grayed section
      The slowness of the receiving process
      The congestion in the network

## Slide 11: Receiving Buffer
The receiving circular buffer is divided into two areas
  White area:
    Empty locations to be filled
  Colored area:
    Contain received bytes that can be consumed by the receiving process

## Slide 12: Segments
TCP groups a number of bytes together into a packet called a segment
  A TCP packet is called a segment
  TCP adds a header to each segment
  Then, the segments are encapsulated in an IP datagram
Note: terms
  UDP: User Datagram, TCP: Segment
  IP: Datagram
  MAC : Frame

## Slide 13
Figure 12-6
TCP Segments
The McGraw-Hill Companies, Inc., 2000

## Slide 14: Full-Duplex Communication
TCP offers full-duplex service
  Data can flow in both directions at the same time
  Each TCP has a sending and receiving buffer and segments are sent in both direction

## Slide 15: Multiplexing and Demultiplexing
TCP
TCP

## Slide 16: Connection-Oriented Service
TCP is a connection-oriented protocol
  However, the connection is virtual, not a physical connection
  Each TCP segment may use a different path to reach the destination

## Slide 17: Reliable Service
TCP uses an acknowledge mechanism to check the safe and sound arrival of data

## Slide 18: Outline
TCP Services
TCP Features
Segment
A TCP Connection
State Transition Diagram
Windows in TCP
Flow Control
Error Control
Congestion Control
TCP Timers
Options
TCP Package

## Slide 19
12.2 TCP FEATURES
To provide the services mentioned in the previous section, TCP has several features that are briefly summarized in this section.
The topics discussed in this section include:
Numbering System
Flow Control
Error Control Congestion Control

## Slide 20: Numbering Bytes
Although TCP use segments for transmission and reception
  There is no field for a segment number in the segment header, i.e., TCP header
TCP uses sequence number and acknowledgement number to keep track of the segment being transmitted or received
  Notably, these two fields refer to the byte number, not the segment number

## Slide 21: Byte Numbers
TCP numbers all data bytes that are transmitted in a connection
The numbering does not necessarily start from 0
  It starts randomly
  Between 0 and 2^32 – 1 for the number of the first byte
  Byte numbering is used for flow and error control

## Slide 22: Sequence Number
TCP assigns a sequence number to each segment
The sequence number for each segment is the number of the first byte carried in that segment

## Slide 23
Suppose a TCP connection is transferring a file of 5000 bytes. The first byte is numbered 10001.
What are the sequence numbers for each segment if data is sent in five segments, each carrying 1000 bytes?
Example 15.1

## Slide 24: Solution
The following shows the sequence number for each segment:
Segment 1 ➡ Sequence Number: 10,001 (range: 10,001 to 11,000)
Segment 2 ➡ Sequence Number: 11,001 (range: 11,001 to 12,000)
Segment 3 ➡ Sequence Number: 12,001 (range: 12,001 to 13,000)
Segment 4 ➡ Sequence Number: 13,001 (range: 13,001 to 14,000)
Segment 5 ➡ Sequence Number: 14,001 (range: 14,001 to 15,000)

## Slide 25: Acknowledgment Number
Each party numbers the bytes, usually with a different starting byte number
  Sequence number: the number of the first byte carried by the segment
  Acknowledgment number: the number of the next byte that the party expects to receive

## Slide 26: Acknowledgment Number (Cont.)
Acknowledgment number is cumulative
For example, if a party uses 5,643 as an acknowledgment number
  It has received all bytes from the beginning up to 5,642
  Note that, this does not mean that the party has received 5642 bytes
    The first byte number does not have to start from 0

## Slide 27: Flow Control
The receiver controls how much data are to be sent by the sender
  Prevent the receiver from being overwhelmed with data
The numbering system allow TCP to use a byte-oriented flow control

## Slide 28: Error Control
TCP implements an error control mechanism
  To provide reliable service
  Also byte-oriented

## Slide 29: Congestion Control
TCP takes into account congestion in the network
Thus, the amount of data sent by a sender is controlled both by
  The receiver (flow control)
  The level of congestion in the network (congestion control)

## Slide 30: Outline
TCP Services
TCP Features
Segment
A TCP Connection
State Transition Diagram
Windows in TCP
Flow Control
Error Control
Congestion Control
TCP Timers
Options
TCP Package

## Slide 31
12.3 SEGMENT
A packet in TCP is called a segment
The topics discussed in this section include:
Format
Encapsulation

## Slide 32
Figure 12-19
TCP Segment Format
The McGraw-Hill Companies, Inc., 2000

## Slide 33: TCP Segment Format
Source port address: 16-bit
Destination port address: 16-bit
Sequence number: 32-bit
  The first byte number in this segment
  In connection establishment, each party randomly generate an initial sequence number (ISN)
    Usually different in each direction
Acknowledgment number: 32-bit
  The byte number that the receiver expects
    If received byte number x, ack. number is x+1
  Acknowledgment and data can be piggybacked together

## Slide 34: TCP Segment Format (Cont.)
Header length: 4-bit
  The number of 4-byte words in the TCP header
  Value of this field is between 5 and 15
    TCP header is between 20-60 bytes
Reserved: 6-bit
  Reserved for future use
Control: 6-bits

## Slide 35
Figure 12-20
Control Field
The McGraw-Hill Companies, Inc., 2000

## Slide 36: TCP Segment Format (Cont.)
Control
  URG: urgent pointer is valid
  ACK: acknowledgment field is valid
  PSH: push the data
  RST: the connection must be reset
  SYN: Synchronization sequence numbers during connection
  FIN: terminate the connection

## Slide 37: TCP Segment Format (Cont.)
Window size: 16-bit
  Define the size of the receiving window, in bytes
    Determined by the receiver
  The maximum window size is 2^16 - 1= 65535
Checksum: 16-bit
  Follow the same procedure as UDP
  Checksum for TCP is mandatory (UDP is optional)
Urgent pointer: 16-bit
  Valid only if the urgent bit is set
  Used when the segment contains urgent data
Options: 0~40 bytes

## Slide 38: Pseudoheader Added to the TCP Datagram

## Slide 39: Encapsulation
A TCP segment is encapsulated in an IP datagram
  Which in turn is encapsulated in a data-link frame

## Slide 40: Outline
TCP Services
TCP Features
Segment
A TCP Connection
State Transition Diagram
Windows in TCP
Flow Control
Error Control
Congestion Control
TCP Timers
Options
TCP Package

## Slide 41
12.4 A TCP CONNECTION
TCP is connection-oriented. A connection-oriented transmission requires three phases: connection establishment, data transfer, and connection termination.
The topics discussed in this section include:
Connection Establishment
Data Transfer
Connection Termination
Connection Reset

## Slide 42: Introduction
TCP is connection-oriented
  Establishes a virtual path.
  All of the segments are then sent over this virtual path.
TCP’s connection-oriented transmission requires three phases
  Connection establishment
    Three-way handshaking
  Data transfer
  Connection termination
    Four-way handshaking

## Slide 43: Connection Establishment
Four actions are taken between host A and B
  Host A sends a segment to announce its wish for connection and includes its initialization information
  Host B sends a segment to acknowledge the request of A
  Host B sends a segment that includes its initialization information
  Host A sends a segment to acknowledge the request of B
However
  Step 2 and 3 can be combined into one step

## Slide 44: Connection Establishment
Example, a client wants to make a connection to a server
  Server performs the passive open
    Tell TCP that it is ready to accept a connection
  Client performs the active open
    Tell TCP that it needs to be connected to the server

## Slide 45: Three-way handshaking
The client sends the first segment, a SYN segment
  Set the SYN flag
  The segment is used for synchronization of sequence number
    Initialization sequence number (ISN)
  If client wants to define MSS, add MSS option
  If client needs a larger window
    Define the window scale factor option
  Does not contain any acknowledgment number
  Does not define the window size either
    A window size makes sense only when a segment includes an acknowledgment
  Although a control segment and does not carry data
    But consumes one sequence number

## Slide 46: Three-way handshaking (Cont.)
The server sends a second segment, a SYN + ACK segment
  Set the SYN and ACK flag
  Acknowledge the receipt of the first segment using the ACK flag and acknowledgment number field
    Acknowledgment number = client initialization sequence number + 1
    Must also define the receiver window size for flow control
  SYN information for the server
    Initialization sequence number from server to client
    Window scale factor if used
    MSS is defined

## Slide 47
Three-way Handshaking
The McGraw-Hill Companies, Inc., 2000
8001

## Slide 48: Three-way handshaking (Cont.)
The client sends the third segment, ACK segment
  Acknowledge the receipt of second segment
    ACK flag is set
      Acknowledgement number = server initialization sequence number + 1
    Must also define the window size
      Set the window size field
    The sequence number is the one in the SYN segment + 1
  However, in some implementation, data can be sent with the third packet
    Must have a new sequence number showing the byte number of the first byte in the data

## Slide 49
An ACK segment, if carrying no data, consumes no sequence number.
A SYN segment cannot carry data, but it consumes one sequence number.
Note
A SYN + ACK segment cannot carry data, but does consume one sequence number.

## Slide 50: Connection Establishment (Cont.)
Active open
  The side that sends the first SYN
Passive open
  The side that receives this SYN and sends the next SYN
Simultaneous open
  Both processes issue an active open
    Improbable occur
    But only a single connection is established.

## Slide 51: SYN Flooding Attack
A malicious attacker sends a larger number of SYN segment to a server
  Each with a fading source IP address
The server will runs out of resource and may crash
  Denial of service attack

## Slide 52: SYN Flooding Attack (Cont.)
Possible solutions
  Impose a limit of connections requested during a period of time
  Filter out datagrams coming from unwanted source addresses
  Postpone resource allocation until the entire connection is set up
    SCTP uses strategy, called cookie
    P.73 in Chapter 16

## Slide 53: Data Transfer
Bidirectional data transfer takes place after connection is established
  Both parties can send data and acknowledgments in both direction
  Piggyback acknowledgment when sending a data segment

## Slide 54
10001

## Slide 55: Pushing Data
In TCP, both sender and receiver have buffers to hold data
  In sender, application data to be sent is temporary hold in the buffer
  In receiver, receiving data is temporary hold in the buffer
  Thus, for applications, they may encounter delayed transmission and reception

## Slide 56
Figure 12-5
Sending and Receiving Buffers
The McGraw-Hill Companies, Inc., 2000

## Slide 57: Pushing Data (Cont.)
In some cases, delayed transmission and reception may not be acceptable
TCP thus support PUSH operation
  Sending TCP must create a segment and send the data immediately
    Must not wait for the window to be filled
  Receiving TCP must deliver data to the application immediately
    Does not wait for more data to come

## Slide 58: Urgent Data
TCP is a stream-oriented protocol
  Data is presented as a stream of bytes
In some cases, an application needs to send urgent data
  Sender wants a piece of data to be read out of order by the receiving application

## Slide 59: Urgent Data (Cont.)
Solution: send a segment with URG bit set
  Sender creates a segment
    Insert the urgent data at the beginning of the segment
    The urgent pointer field defines the end of the urgent data and the start of normal data
    Send the segment with the URG bit set

## Slide 60: Connection Termination
Two options
  Three-way handshaking
  Four-way handshaking with a half-close option
    By calling shutdown() with a second argument of 1
      Instead of calling close()

## Slide 61: Three-Way Handshaking
Client TCP sends the FIN segment
  FIN flag is set
  Two choices
    FIN segment is only a control segment
      Consume only one sequence number
    FIN segment can include the last chunk of data sent by the client

## Slide 62: Three-Way Handshaking (Cont.)
The server TCP sends the FIN+ACK segment
  ACK bit is set
    Confirm the receipt of FIN segment
  FIN bit is set
    Announce the closing of the connection in the other direction
  Two choices
    FIN+ACK segment is only a control segment
      Consume only one sequence number
    FIN +ACK segment can include the last chunk of data sent by the server

## Slide 63
Three-Way Handshaking
The McGraw-Hill Companies, Inc., 2000
x+1

## Slide 64: Three-Way Handshaking (Cont.)
3. Client TCP sends the last ACK segment
  ACK bit is set
    Confirm the receipt of the FIN+ACK segment for the TCP server
  This segment cannot carry data and consume no sequence number
    No further response!

## Slide 65: Four-Way Handshaking with Half-Close
Host A sends a FIN segment announcing its wish for connection termination
Host B sends a ACK segment acknowledging the FIN segment from A
  The connection is closed in one direction
  But host B can continue sending data to A
Host B sends a FIN segment to close the connection
Host A sends a ACK segment to acknowledges the FIN segment from B

## Slide 66
Half-Close
y
x+1
z+1
x+1

## Slide 67: Connection Reset
The TCP at one end may
  Deny a connection request
  Abort a connection
  Terminate an idle connection
How to achieve ?
  By the RST (reset) flag

## Slide 68: Denying a Connection
Example
  A TCP segment is received and requested a connection to a nonexistent port
  The receiving TCP sends a segment with the RST bit set

## Slide 69: Aborting a Connection
A process may want to abort a connection instead of closing it normally
  Example, the process does not want the data in the queue to be sent
    If closed normally, the data will be sent

## Slide 70: Terminate an Idle Connection
TCP on one side may discover that the TCP on the other side has been idle for a long time
Send an RST segment to destroy the connection

## Slide 71: Outline
TCP Services
TCP Features
Segment
A TCP Connection
State Transition Diagram (Skip!)
Windows in TCP
Flow Control
Error Control
Congestion Control
TCP Timers
Options
TCP Package

## Slide 72
12.5 STATE TRANSITION DIAGRAM
To keep track of all the different events happening during connection establishment, connection termination, and data transfer, the TCP software is implemented as a finite state machine. .
The topics discussed in this section include:
Scenarios

## Slide 73
Figure 12-30
State Transition Diagram
The McGraw-Hill Companies, Inc., 2000

## Slide 74: Outline
TCP Services
TCP Features
Segment
A TCP Connection
State Transition Diagram
Windows in TCP
Flow Control
Error Control
Congestion Control
TCP Timers
Options
TCP Package

## Slide 75: Windows in TCP
TCP uses two windows for each direction
  Send window
  Receive window
Thus, four windows for a bidirectional communication in TCP
The windows in TCP number bytes

## Slide 76: Send Window

## Slide 77
Figure 12-5
Sending and Receiving Buffers
The McGraw-Hill Companies, Inc., 2000

## Slide 78: Send Window (Cont.)
A send window can open, close, or shrink
  Detailed are introduced later

## Slide 79: Receive Window
The receive window size, rwnd is calculated as:
  As shown in the figure (a) of the next slide
A receive can open and close
  It should never shrink
  As shown in the next slide
Open: moves its right wall to the right
  When more bytes are pulled by the process
Close: moves its left wall to the right
  When more bytes arrive from the sender
rwnd = buffer size – number of waiting bytes to be pulled

## Slide 81: Outline
TCP Services
TCP Features
Segment
A TCP Connection
State Transition Diagram
Windows in TCP
Flow Control
Error Control
Congestion Control
TCP Timers
Options
TCP Package

## Slide 82
12.6 FLOW CONTROL
Flow control regulates the amount of data a source can send before receiving an acknowledgment from the destination. TCP defines a window that is imposed on the buffer of data delivered from the application program.
The topics discussed in this section include:
Sliding Window Protocol
Silly Window Syndrome

## Slide 83: Flow Control
Balance the rate a producer creates data with the rate a consumer can use the data
Solution: the sliding window protocol by TCP
  Both hosts use a window for each connection
  Called sliding windows
    The window can slide over the buffer
  TCP’s sliding windows are byte oriented

## Slide 84
Figure 12-5
Sending and Receiving Buffers
The McGraw-Hill Companies, Inc., 2000

## Slide 85: Sliding Window Protocol (Cont.)
The window is opened, closed, or shrunk
Opening a window
  Moving the right wall to the right
Closing a window
  Moving the left wall to the right
Shrinking the window
  Moving the right wall to the left

## Slide 86: Sliding Window Protocol (Cont.)
The size of the window at one end is determined by the minimum of two values
  Receiver window (rwnd)
    Advertised by the opposite end in a segment containing acknowledgement
  Congestion window (cwnd)
    Determined by the network to avoid congestion
    Discussed later

## Slide 87
Figure 12-11
Sliding Window in the Sending TCP
The McGraw-Hill Companies, Inc., 2000
IP
data has been sent and acked

## Slide 88: Example A
Suppose that Receiver B:
  Buffer size = 5000
  Receive 1000 bytes unprocessed data
  What is the value of the receiver window (rwnd) for sender A?
Solution
  The value of rwnd = 5,000 − 1,000 = 4,000.
  Host B can receive only 4,000 bytes of data before overflowing its buffer.
  Host B advertises this value in its next segment to A.

## Slide 89: Example B
Suppose sender A:
  rwnd = 3000 bytes
  cwnd = 3500 bytes
  What is the size of the window for host A?
Solution
  The size of the window is the smaller of rwnd and cwnd
  Ans: 3,000 bytes

## Slide 90: Example C: Figure 12.21 shows an unrealistic example of a sliding window
The sender has sent bytes up to 202.
cwnd = 20 (in reality this value is thousands of bytes).
The receiver has sent a ACK segment
  Acknowledgment number = 200
  rwnd = 9 bytes (in reality this value is thousands of bytes).
Therefore
  The size of the sender window
    The minimum of rwnd and cwnd or 9 bytes.
  Bytes 200 to 202 are sent, but not acknowledged.
  Bytes 203 to 208 can be sent without worrying about acknowledgment.
  Bytes 209 and above cannot be sent.

## Slide 91
Figure 12-11
Figure 12.21
The McGraw-Hill Companies, Inc., 2000

## Slide 92: Example D
In Figure 12.21
  Server receives a packet
    Acknowledgment value = 202
    rwnd = 9.
  The host has already sent bytes 203, 204, and 205.
  The value of cwnd is still 20.
  Show the new window.

## Slide 93: Example D (Cont.)
Solution
  Figure 12.22 shows the new window.
  Note that this is a case in which the window
    Closes from the left and opens from the right by an equal number of bytes
    The size of the window has not been changed.
  The acknowledgment value, 202, declares that bytes 200 and 201 have been received

## Slide 94
Figure 12-11
Figure 12.22
The McGraw-Hill Companies, Inc., 2000

## Slide 95: Example E
In Figure 12.22
  Sender receives a packet
    Acknowledgment value = 206
    rwnd = 12.
  The host has not sent any new bytes.
  The value of cwnd is still 20.
  Show the new window.

## Slide 96: Example E (Cont.)
Solution
  rwnd < cwnd
    The size of the window is 12.
  Figure 12.23 shows the new window.
    The window has been opened from the right by 7 and closed from the left by 4
    The size of the window has increased.

## Slide 97
Figure 12-11
Figure 12.23
The McGraw-Hill Companies, Inc., 2000

## Slide 98: A Scenario: An example of flow control (As Shown in the Next Figure)
1. SYN segment
  Client announces its initial seq. number = 100
  When server receives, assume that the server allocates a buffer size of 800
2. ACK+SYN
  The client also announces a buffer size of 800
3. ACK
4. The client process pushes 200 bytes of data
  Number from 101 to 300 and send this segment
5. Send ACK from server to client
6. The client process again push 300 more bytes
  A new segment: seqNo=301, length = 300 bytes
  Assume that the server process also pulled 100 bytes of data
  Thus, the receiver window only reduce 200 bytes
7, 8. ACK from the server to the client

## Slide 100: Shrinking of Windows
The receiver never shrink
But the sender window can shrink on occasion
  If the receiver defines a value for rwnd that results in shrinking the window
  Some implementations do not allow

## Slide 101
Example 15.2
Figure 15.26 shows the reason in window shrinking.
Part a shows values of last acknowledgment and rwnd.
Part b shows the situation in which the sender has sent bytes 206 to 214. Bytes 206 to 209 are acknowledged and purged.
  The new advertisement, however, defines the new value of rwnd as 4, in which 210 + 4 < 206 + 12.
  When the send window shrinks, it creates a problem: byte 214 which has been already sent is outside the window.
Solution:
  Let the receiver postpone its feedback until enough buffer locations are available in its window.
  In other words, the receiver should wait until more bytes are consumed by its process.

## Slide 102
210

## Slide 103: Solution of Shrinking the Window
How can the receiver avoid shrinking the window in the example 15.2?

## Slide 104: Example 9 (Cont.)
Solution:
  The receiver needs to keep track of the last acknowledgment number and the last rwnd.
    Right wall = acknowledgment number + rwnd
  To prevent shrinking, we must always have the following relationship.
new ack + new rwnd ≥ last ack + last rwnd or new rwnd ≥ (last ack + last rwnd) − new ack

## Slide 105: Example 9 (Cont.)
In example 8
  New Ack. Num. = 216, New rwnd = 4
  Last Ack. Num = 206, Last rwnd = 12
  210+4 < 206+12; the relationship is not hold
Thus, the receiver must want until more buffer space is free before sending an ack.
  i.e., have a larger value of rwnd

## Slide 106: Window Shutdown
In some cases, the receiver does not want to receive any data from the sender for a while
  The receiver temporarily shut down the window
  Sending a segment with the rwnd = 0
  The sender stops until a new advertisement has arrived
However, during window shutdown
  The sender can always send a segment with one byte of data
  Called probing and is used to prevent deadlock

## Slide 107
Some Points about TCP’s Sliding Windows
  The size of the window is the lesser of rwnd and cwnd
  The source does not have to send a full window’s worth of data
  The send window can be opened or closed by the receiver, but should not be shrunk
  The destination can send an acknowledgment at any time as long as it does not result in a shrinking window
  The receiver can temporarily shut down the window; the sender, however, can always send a segment of one byte after the window is shut down

## Slide 108: Silly Window Syndrome
Problem in the sliding window operation
  The sending process creates data slowly
  Or the receiving process consume data slowly
  Or both
  Result in the sending of data in very small segment
    Reduce the network efficiency
For example, send a one byte segment result in overhead of 41/1
  Assume TCP header is 20 bytes + IP header is 20 bytes

## Slide 109: Syndrome Created by the Sender
Sender application create data too slowly
  For example, only 1 byte at a time
  Sending TCP would create segments containing 1 byte of data
Solution: prevent the sending TCP from sending the data byte by byte
  Sending TCP must be forced to wait as it collects data to send in a larger block
  But, how long should the sending TCP wait?

## Slide 110: Nagle’s Algorithm
Nagle found the solution to above syndrome
  The sending TCP sends the first piece of data it receives from the sending application
    Even if it is only 1 byte
  After sending the first segment, the sending TCP accumulates data in the buffer and wait until
    Either the receiving TCP sends an acknowledge
    Or until enough data has accumulated to fill a maximum-sized segment
  Step 2 is repeated. Segment 3 is sent if an acknowledgment is received for segment 2 or enough data is accumulated to fill a maximum-size segment

## Slide 111: Nagle’s Algorithm (Cont.)
Elegance
  Very simple
  Take into account the speed of the application that creates the data and the speed of the network that transports the data
    If application is faster than the network
      The segments are larger
    If the application is slower than the network
      The segment are smaller

## Slide 112: Syndrome Created by the Receiver
The receiving TCP may also create a silly window syndrome
  If it is serving an application that consumes data slowly
For example
  Sender application create data in 1K byte blocks
  But the receiving application consumes data 1 byte at a time
  Assume the receiver buffer is 4K bytes
    Buffer will be full soon
    Sender then only can send 1 byte data to the receiver

## Slide 113: Syndrome Created by the Receiver (Cont.)
Solution
  Clark’s solution
  Delayed acknowledgment

## Slide 114: Clark’s Solution
Send an acknowledgment as soon as the data arrives but to announce a window size of zero until
  Either there is enough space to accommodate a segment of maximum size
  Or half of the buffer is empty

## Slide 115: Delayed Acknowledgment
Delay sending the acknowledgment
  When a segment arrives, it is not acknowledged immediately
  Receiver waits until there is a decent amount of space in its incoming buffer
Delayed acknowledgment prevents the sending TCP from sliding it window

## Slide 116: Delayed Acknowledgment (Cont.)
Another advantage
  Reduce traffic
  The receiver does not have to acknowledge each segment
Disadvantage
  The sender may retransmit the unacknowledged segment
Solution
  Defines the acknowledgment should not be delayed by more than 500 ms

## Slide 117: Outline
TCP Services
TCP Features
Segment
A TCP Connection
State Transition Diagram
Windows in TCP
Flow Control
Error Control
Congestion Control
TCP Timers
Options
TCP Package

## Slide 118
12.7 ERROR CONTROL
TCP provides reliability using error control, which detects corrupted, lost, out-of-order, and duplicated segments. Error control in TCP is achieved through the use of the checksum, acknowledgment, and time-out.
The topics discussed in this section include:
Checksum
Acknowledgment
Retransmission
Out-of-Order Segments
Some Scenarios

## Slide 119: Error Control
TCP provides reliability using error control
  Detect corrupted segment, lost segment, out-of-order segment, and duplicated segment
Error detection and correction is achieved by
  Checksum
  Acknowledgment
  Time-out

## Slide 120: Checksum
TCP uses 16-bit checksum
  Mandatory in every segment
Actually, 16-bit checksum is considered inadequate for SCTP
  Mentioned later

## Slide 121: Acknowledgment
TCP uses acknowledgment to confirm the receipt of data segment
Control segments that carry no data but consume a sequence number are also acknowledged
ACK segment are never acknowledged

## Slide 122: Acknowledgment Type
Acknowledgment type
  Accumulative Acknowledgment (ACK)
    In past, TCP only uses this ACK
  Selective Acknowledgment (SACK)
    Newly added feature

## Slide 123: Accumulative Acknowledgment (ACK)
The receiver advertises the next byte it expects to receive
  Ignore all segments received out-of-order
Also called “positive” accumulative acknowledgement
  Discarded, lost, or duplicated segments are not reported

## Slide 124: Selective Acknowledgment (SACK)
Does not replace ACK
But report additional information to the sender
  The block of data that is out-of-order
  The block of segments that is duplicated
SACK is implemented as an option
  Since there is no provision in the TCP header for SACK

## Slide 125
Figure 12-19
TCP Segment Format
The McGraw-Hill Companies, Inc., 2000

## Slide 126: Generating Acknowledgments: When Does a Receiver Generate Acknowledgment?
When one end sends a data segment
  It must piggyback an acknowledgment
  Decrease the number of segments needed
The receiver delays sending an ACK
  When the following three conditions hold
    When the receiver has no data to send
    It receives an in-order segment
    The previous segment has already been acknowledged
  The receiver delays sending an ACK
    until another segment arrives or
    Until a period of time (normally 500 ms) has passed
  Thus, if only one outstanding in-order segment
    Delaying sending an ACK
  Prevent ACK segments from creating extra traffic

## Slide 127: Generating Acknowledgments: When Does a Receiver Generate Acknowledgment? (Cont.)
The receiver immediately sends an ACK
  When the following two conditions hold
    An in-order segment arrives
    The previous in-order segment has not been acknowledged
  Thus, there should not be more than two in-order unacknowledged segment at any time
  Prevent unnecessary retransmission

## Slide 128: Generating Acknowledgments: When Does a Receiver Generate Acknowledgment? (Cont.)
The receiver immediately sends an ACK
  When an out-of-order segment with higher sequence number is received
  Enable fast retransmission of any missing segment
When a missing segment arrives, the receiver sends an ACK
  Inform the sender that segments reported missing have been received
The receiver immediately sends an ACK if a duplicate segment arrives
  Solve some problems when an ACK segment itself is lost

## Slide 129: Retransmission
When to retransmit a segment
  When a retransmission timer expires: TCP Tahoe
  When the sender receives three duplicate ACK: TCP Reno
No retransmission occurs for segments
  If it does not consume sequence number
  If it is an ACK segment

## Slide 130: Retransmission After RTO
Sender TCP starts a retransmission time-out (RTO) timer for each segment sent
If timer matures
  Retransmit the segment
RTO value is dynamic
  Updated based on the round trip time (RTT)

## Slide 131: Retransmission After Three Duplicated ACK Segments
A segment is lost but the receiver receives so many out-of-order segments
  Buffer may overflow
Solution: fast retransmission
  Retransmit the missing segment immediately if three duplicate ACK received

## Slide 132: Out-of-Order Segment
Out-of-order
  When a segment is delayed, lost, or discarded
Previous solution in TCP
  Does not acknowledge an out-of-order segment
  Discard all out-of-order segment
    Result in the retransmission of the missing segment and the following segment

## Slide 133: Out-of-Order Segment (Cont.)
Current implementation of TCP
  Store out-of-order segments temporarily
  Until the missing segment arrives
Note
  The out-of-order segment are not delivered to the process
  TCP guarantees in-order delivery

## Slide 134
Data may arrive out of order and be temporarily stored by the receiving TCP,
but TCP guarantees that no out-of-order data are delivered to the process.
Note

## Slide 135: Some Scenarios
Some scenarios occurs during the operation of TCP
  Normal operation
  Lost segment
  Fast retransmission
  Delayed segment
  Duplicate segment
  Automatically corrected lost ACK
  Lost acknowledgment corrected by resending a segment
  Deadlock created by lost acknowledgment

## Slide 136
Figure 12-13
Normal Operation
The McGraw-Hill Companies, Inc., 2000
Wait to see if more segments arrives

## Slide 137: Lost or Corrupted Segment
A lost or corrupted segment is treated the same way by the receiver TCP
  Lost segment: discarded somewhere in the network
  Corrupted segment: discarded by the receiver itself
In following feature, segment 3 is lost
  Receiver receives a out-of-order segment (segment 4)
    Store it temporary and leave a gap
    Send an ACK immediately (ACK number = 701)
  Sender resent segment 3 when the RTO timer matures

## Slide 138: Lost Segment
Rule 3

## Slide 139: Fast Retransmission
In the following feature
  When the receiver receives the 4th, 5th, 6th segment, it triggers an acknowledgment
  Thus, four acknowledgment are the same value
    Three duplicated
  Although the RTO timer for segment 3 has not yet matured
    Invoke fast retransmit for segment 3

## Slide 140
Figure 12-14
Fast Retransmission
The McGraw-Hill Companies, Inc., 2000

## Slide 141: Delayed Segment
Each TCP segment is encapsulated in an IP datagram
  IP datagram is routed independently
  A TCP segment may be delayed
A delayed segment is treated the same way as lost or corrupted segment by the receiver
Note
  A delayed segment may arrive after it has been resent
  Cause a duplicate segment

## Slide 142: Duplicate Segment
Created by a sending TCP when a segment is delayed and treated as lost by the receiver
Destination detects duplicate segment since they have the same sequence number
  Discard the later segment

## Slide 143: Automatically Corrected Lost ACK
A lost acknowledgment is automatically replaced by the next
  Since ACK is accumulative
In the following feature
  The next ACK automatically correct the lost of the acknowledgment

## Slide 144
Figure 12-13
Lost Acknowledgment
The McGraw-Hill Companies, Inc., 2000

## Slide 145: Lost Acknowledgment Corrected by Resending a Segment
If an ACK is lost
  But the next ACK is delayed for a long time or
  There is no next acknowledgment
How to correct ?
  By the RTO timer and resent the data segment
Result in a duplicate ACK
  Receiver just discards it
  Resent the ACK immediately (rule 6)

## Slide 146
Figure 12-14
Lost Acknowledgment Corrected by Resending a Segment
The McGraw-Hill Companies, Inc., 2000

## Slide 147: Deadlock Created by Lost Acknowledgment
A lose of an acknowledgment may result in system deadlock
Example
  Receiver sends an ACK with rwnd = 0
    Request the sender to shut down its window temporarily
  The sending TCP stops transmitting segments
  After a while, receiver sends an ACK and rwnd <>0
    Announce it can receive data again
    However, this ACK is lost
  As a result, both sender and receiver continue to wait for each other forever
Solution: a persistent timer

## Slide 148: Outline
TCP Services
TCP Features
Segment
A TCP Connection
State Transition Diagram
Windows in TCP
Flow Control
Error Control
Congestion Control
TCP Timers
Options
TCP Package

## Slide 149
12.8 CONGESTION CONTROL
Congestion control refers to the mechanisms and techniques to keep the load below the capacity.
The topics discussed in this section include:
Congestion Window
Congestion Policy

## Slide 150: Congestion Control in TCP
Outline
  Congestion window
  Congestion policy
    Slow start: exponential increase
    Congestion avoidance: additive increase
    Congestion detection: multiplicative decrease

## Slide 151: Congestion Window
Flow control
  Sender window size is determined by the available buffer space in the receiver
However, in addition to the receiver, the network should be a second entity that determines the size of the sender’s window
Congestion control
  Determine the sender window size by the congestion condition in the network

## Slide 152: Congestion Window (Cont.)
Thus, the sender’s window size is determined by both
  Receiver
  Congestion in the network
The sender has two pieces of information
  The receiver-advertised window size
  The congestion window size
The actual size of the window is the minimum of these two
  Actual window size
  = minimum (receiver window size, congestion window size)
  = minimum (rwnd, cwnd)

## Slide 153: Congestion Policy
Three phase in TCP’s congestion policy
  Slow start
  Congestion avoidance
  Congestion detection
    When a congestion is detected, sender return to the slow start or congestion avoidance

## Slide 154: Slow Start: Exponential Increase
At the beginning,
  Congestion window size = maximum segment size (MSS)
Each time on acknowledgement arrives
  Increase the congestion window size by one MSS
  Until it reaches a threshold, called ssthresh (slow start threshold)
    Usually, ssthresh = 65535 bytes

## Slide 155: Slow Start: Exponential Increase (Cont.)
However, it is not actually “slow start”
  The congestion window size increases exponentially
  Start => cwnd = 1 = 2^0
  After 1 RTT => cwnd = 2 = 2^1
  After 2 RTT => cwnd = 4 = 2^2
  After 3 RTT => cwnd = 8 = 2^3

## Slide 156
Slow Start: Exponential Increase
The McGraw-Hill Companies, Inc., 2000

## Slide 157: Slow Start: Exponential Increase (Cont.)
However, slow start is slower in the case of delayed acknowledgments
Remember, for each ACK, the cwnd is increased by 1 MSS
Thus, if two segments are acknowledged accummlatively
  cwnd is increased by one

## Slide 158: Congestion Avoidance: Additive Increase
Started after the congestion window size reaches the ssthresh threshold
When the whole window of segments is acknowledged
  The size of congestion window is increased one
  Note, the whole window size is usually larger than one in congestion avoidance

## Slide 159
Figure 12-14
Congestion Avoidance, Additive Increase
The McGraw-Hill Companies, Inc., 2000

## Slide 160: Congestion Avoidance: Additive Increase (Cont.)
In the above figure
  Start => cwnd = i
  After 1 RTT => cwnd = i + 1 = 2
  After 2 RTT => cwnd = i + 1 = 3
  After 3 RTT => cwnd = i + 1 = 4

## Slide 161
In the congestion avoidance algorithm the size of the congestion window
increases additively until
congestion is detected.
Note

## Slide 162: Congestion Detection: Multiplicative Decrease
If congestion occurs, the congestion window size must be decreased
How to detect a congestion?
  The need to retransmit a segment
  Assume by TCP that a packet is dropped by a router
When to retransmit a segment
  When an RTO timer out
  When three duplicate ACKs are received

## Slide 163: Congestion Detection: Multiplicative Decrease (Cont.)
In both cases, the size of the threshold is half of the current congestion window size
  multiplicative decrease
However, different actions are taken
  If a time-out occurs: a strongly possibility of congestion
    The threshold should be set to half of the current congestion window size
      Multiplicative decrease
    The congestion window size should start from one again, i.e., cwnd = 1
    The sender return to the slow start phase

## Slide 164: Congestion Detection: Multiplicative Decrease (Cont.)
  2. If three duplicated ACKs are received: a weaker possibility of congestion
  Invoke fast retransmission and fast recovery
    The threshold should be set to half of the current congestion window size
      Multiplicative decrease
    The congestion window size = threshold again, i.e., cwnd = ssthresh
    The sender starts the congestion avoidance phase

## Slide 165
Figure 12-17
TCP Congestion Policy Summary
The McGraw-Hill Companies, Inc., 2000

## Slide 166
Figure 12-17
Congestion Example
The McGraw-Hill Companies, Inc., 2000

## Slide 167: Outline
TCP Services
TCP Features
Segment
A TCP Connection
State Transition Diagram
Windows in TCP
Flow Control
Error Control
Congestion Control
TCP Timers
Options
TCP Package

## Slide 168
12.9 TCP TIMERS
To perform its operation smoothly, most TCP implementations use at least four timers.
The topics discussed in this section include:
Retransmission Timer
Persistence Timer
Keepalive Timer
TIME-WAIT Timer

## Slide 169
Figure 12-16
TCP Timers
The McGraw-Hill Companies, Inc., 2000

## Slide 170: Retransmission Timer
When TCP sends a segment, it creates a retransmission timer to that segment
  If an acknowledgment is received before the timer goes off
    The timer is destroyed
  If timer goes off before an acknowledgment arrives
    The segment is retransmitted and the timer is reset

## Slide 171: Calculation of Retransmission Timer
TCP cannot use the same retransmission timer for all connections
  Each connection has different length and network characteristics
Furthermore, TCP cannot use the same retransmission timer for one single connection
  The network behavior is dynamic
Thus, TCP uses the dynamic retransmission timer
  Different for each connection and may be changed during the same connection

## Slide 172: Calculation of Retransmission Time (Cont.)
Retransmission time-out (RTO) is calculated based on RTT
But, how to calculate RTT?

## Slide 173: Calculation of RTT
Measured RTT
Smoothed RTT
RTT Deviation

## Slide 174: Measured RTT
Measured RTT: RTTM
  How long it takes to send a segment and receive an acknowledgment
Note, segments and their ACKs do not have a one-to-one relationship
  Several segments may be acknowledged together
In TCP, only one RTT measurement can be in process at any time

## Slide 175: Smoothed RTT
The measured RTT may fluctuation very highly
  Cannot be used for RTO purpose
Smooth RTT: RTTS
RTTS = (1-a) RTTS + a x RTTM
  a is usually 1/8 percent

## Slide 176: RTT Deviation
Most implementation also calculate the RTT deviation, called RTTD
Initially => No value
After first measurement
  RTTD = RTTM/2
After any other measurement
  RTTD=(1-B)RTTD+Bx |RTTS-RTTM|
  B is usually 1/4

## Slide 177: Retransmission Timeout (RTO)
Original => Initial value
After any measurement
  RTO = RTTS + 4 x RTTD

## Slide 178
Figure 12.38 shows part of a connection. The figure shows the connection establishment and part of the data transfer phases.
Example 15.3
1. When the SYN segment is sent, there is no value for RTTM , RTTS , or RTTD . The value of RTO is set to 6.00 seconds.
RTO = 6
2. When the SYN+ACK segment arrives, RTTM is measured and is equal to 1.5 seconds.
RTTM = 1.5 RTTS = 1.5 RTTD = 1.5 / 2 = 0.75 RTO = 1.5 + 4 . 0.75 = 4.5

## Slide 179
Example 15.3 (continued)
3.When the first data segment is sent, a new RTT measurement starts. Note that the sender does not start an RTT measurement when it sends the ACK segment, because it does not consume a sequence number and there is no time-out. No RTT measurement starts for the second data segment because a measurement is already in progress.
RTTM = 2.5 RTTS = 7/8 (1.5) + 1/8 (2.5) = 1.625 RTTD = 3/4 (0.75) + 1/4 |1.625 − 2.5| = 0.78 RTO = 1.625 + 4 (0.78) = 4.74

## Slide 181: Karn’s Algorithm
Problem
  If a segment is not acknowledged during the retransmission timer period and it is retransmitted
  When the sending TCP receives an ACK.
    It does not know this acknowledgment is for the first one or for the retransmitted one?
Solution: Karn’s algorithm
  Do not consider the RTT of a retransmitted segment in the calculation of the new RTT

## Slide 182: Exponential Backoff
What is the value of RTO if a retransmission occurs ?
Exponential backoff in TCP
  RTO is double for each retransmission

## Slide 183
Next Figure is a continuation of the previous example
There is retransmission and Karn’s algorithm is applied.
The first segment in the figure is sent, but lost.
  The RTO timer expires after 4.74 seconds.
  The segment is retransmitted and the timer is set to 9.48, twice the previous value of RTO.
This time an ACK is received before the time-out.
  Wait until we send a new segment and receive the ACK for it before recalculating the RTO (Karn’s algorithm).
Example 15.4

## Slide 185: Persistence Timer
TCP needs another timer to deal with the zero window-size advertisement
Example
  Receiving TCP announces a window size of zero
  The sending TCP stops transmitting segments
  After a while, receiving TCP sends an acknowledgment announcing a non-zero window size
    However, this acknowledgment was lost
  As a result, both sender and receiver continue to wait for each other forever

## Slide 186: Persistence Timer (Cont.)
Solution: TCP uses a persistence timer for each connection
When the sending TCP receives an acknowledgment with a window size of zero
  It starts a persistence timer
When the timer goes off
  The sending TCP sends a special segment called a probe
    Contain only 1 byte of data and is never acknowledged
    Alert the receiving TCP that the acknowledgment may be lost and should be resent

## Slide 187: Persistence Timer (Cont.)
Value of persistence timer is set to the value of the retransmission timer
However, if a response is not received from the receiver
  Another probe segment is sent
  The value of the persistence timer is double
Above process is repeated until the persistence timer reaches a threshold
  Usually 60 seconds

## Slide 188: Keepalive Timer
If a client has crashed
  A TCP connection will be remain open forever
Solution: Keepalive timer
  The time-out is usually 2 hours
  If a server does not hear from the client after two hours
    Send a probe segment
  If there is no response after 10 probes, each of which is 75 seconds apart
    It assumes that client is down and terminates the connection

## Slide 189: Time-Waited Timer
Used during connection termination
Mentioned later but ignore

## Slide 190: Outline
TCP Services
TCP Features
Segment
A TCP Connection
State Transition Diagram
Windows in TCP
Flow Control
Error Control
Congestion Control
TCP Timers
Options
TCP Package (Skip!)

## Slide 191
Figure 12-19
TCP Segment Format
The McGraw-Hill Companies, Inc., 2000

## Slide 192
Figure 12-21
Options
The McGraw-Hill Companies, Inc., 2000

## Slide 193: No Operation
Used to align the next option on a 32-bit boundary

## Slide 194
Figure 12-23
No operation Option
The McGraw-Hill Companies, Inc., 2000

## Slide 195: End of Option
Used for padding at the end of the option field
  Can only be used as the last option
  Can be used only once
Only one end of option can be used
  If more than 1 byte is needed to align the option field, use some no-operation option followed by an end of option
Two pieces of information to the destination
  No more options in the header
  Data from the application program starts at the beginning of the next 32-bit word

## Slide 196
Figure 12-22
End of option Option
The McGraw-Hill Companies, Inc., 2000

## Slide 197: Maximum Segment Size (MSS)
Define the size of the biggest chunk of data that can be received by the destination
Notably, it actually defines the maximum size of data, not the maximum size of segment
Determined during the connection establishment phase
  Once determined, it does not change during the connection
  If neither party defines the size, the default is chosen
  Default value is 536

## Slide 198
Figure 12-24
Maximum segment size Option
The McGraw-Hill Companies, Inc., 2000

## Slide 199: Window Scale Factor
The window size field in the header defines the size of the sliding window
  The size of the windows: 0 ~ 65535
  However, it may not be sufficient in some networks
To increase the window size, the window scale factor is used
  New window size = window size defined in the header x 2window scale factor
However, the window size cannot be greater than the maximum value for the sequence number

## Slide 200: Window Scale Factor (Cont.)
Window scale factor can be determined only during the connection setup phase
Thus, during data transfer, the size of the window may be changed
  But it must be multiplied by the same scale factor
  Cannot be changed during the connection
The scale factor is also called shift count
  Multiplying a number by power of 2 = left shift

## Slide 201
Figure 12-25
Window scale factor Option
The McGraw-Hill Companies, Inc., 2000

## Slide 202: Timestamp
Two applications
  Measure the round trip time
  Prevent wrap around sequence number

## Slide 203
Figure 12-26
Timestamp Option
The McGraw-Hill Companies, Inc., 2000

## Slide 204: Measuring RTT
Timestamp value field
  Filled by the source when a segment leaves
Timestamp echo reply field
  When destination sends an acknowledgement, copy the received timestamp value into the timestamp echo reply field
The source, when it receives acknowledgment
  Calculate the round-trip time
Thus, there is no need for clock synchronization
  All calculation is based on the sender clock

## Slide 205: Measuring RTT (Cont.)
The receiver needs to keep two variables
  lastack: the value of the last acknowledgment number sent
  tsrecent: the value of recent timestamp that has not yet echoed
  Detailed operation is shown in the next example

## Slide 206
The sender simply inserts the value of its system clock in the timestamp field for the first and second segment.
When an acknowledgment comes (the third segment)
  The value of the clock is checked and the value of the echo reply field is subtracted from the current time.
  RTT is 12 s in this scenario.
Example 15.5

## Slide 207
The receiver’s function is more involved.
It keeps track of the last acknowledgment sent (12000).
When the first segment arrives (bytes 12000 to 12099)
  The first byte is the same as the value of lastack.
  Copy the timestamp value (4720) into the tsrecent variable.
When the second segment arrives
  None of the byte numbers in this segment include the value of lastack
    The value of the timestamp field is ignored.
When the receiver decides to send an accumulative acknowledgment with acknowledgment 12200
  Changes the value of lastack to 12200
  Inserts the value of tsrecent in the echo reply field.
Example 15.5 (Continued)

## Slide 209
In this example
  RTT is calculated the time difference between sending the first segment and receiving the third segment.
This is actually the meaning of RTT:
  The time difference between a packet sent and the acknowledgment received.
Example 15.5 (Continued)

## Slide 210: PAWS
Timestamp is also used for another application
  Protection against wrapped around sequence number (PAWS)
Although sequence number is 32 bits
  It could be wrapped around in a high-speed connection
  T=0, a sequence number is n
  After T=t, the sequence number is also n in the same connection

## Slide 211: PAWS (Cont.)
Problem:
  If the fist segment is duplicated and arrives during the second round of sequence number
  The segment will be wrongly considered belonging to the second run
Solution:
  Increase the size of sequence number
    Change the window size and segment format
  Include the timestamp
    The identity of a segment is the combination of timestamp and sequence number

## Slide 212: SACK-Permitted and SACK Options
TCP’s ACK is accumulative
Problems
  Does not report the bytes that have arrived out of order
  Does not report about duplicate segments
Solutions
  Selective acknowledgment (SACK)
Thus, two new options
  SACK permitted
  SACK

## Slide 213: SACK

## Slide 214: SACK-Permitted Option
Two bytes used only during connection establishment
  Not allowed during the data transfer phase
Sender
  SYN segment with SACK-permitted option
Receiver
  SYN+ACK segment also with SACK-permitted option

## Slide 215: SACK Option
Variable length
Include a list of blocks arriving out-of-order
  The first block can also be used to report the duplicates
  Each block occupies two 32-bit number
    Defining the beginning and the end of the block
  SACK option cannot define more than 4 blocks
    The allowed size of an option in TCP is 40 bytes
    If 5 blocks, (5 x 2) x 4 + 2 = 42 > 40

## Slide 216
The first and second segments are in consecutive order.
Segments 3, 4, and 5 are out of order
  A gap between the second and third
  Another gap between the fourth and the fifth.
An ACK and a SACK together can easily clear the situation for the sender.
  The value of ACK is 2001
    Sender need not worry about bytes 1 to 2000.
  The SACK has two blocks.
    The first block announces that bytes 4001 to 6000 have arrived out of order.
    The second block shows that bytes 8001 to 9000 have also arrived out of order.
    This means that bytes 2001 to 4000 and bytes 6001 to 8000 are lost or discarded.
      The sender can resend only these bytes.
Example 15.6

## Slide 217
An end has received five segment of data
Example 15.6 (Continued)

## Slide 218
Figure 12.49 shows how a duplicate segment can be detected with a combination of ACK and SACK.
In the figure, we have two out-of-order segments (in one block) and one duplicate segment.
  SACK uses the first block to show the duplicate data
    Note that only the first block can be used for duplicate data.
  The other blocks to show out-of-order data.
Example 15.7

## Slide 219
Example 15.7 (Continued)

## Slide 220
The example shows what happens if one of the segments in the out-of-order section is also duplicated.
One of the segments (4001:5000) is duplicated.
  The SACK option announces this duplicate data first
  Then the out-of-order block.
Example 15.8

## Slide 221
Example 15.8 (Continued)

## Slide 222: 範圍：CHAPTER 11~15 日期：6/17
第三次考試