## Slide 1: Chapter 3 Underlying Technologies

## Slide 2: Internet Model
Internet is a set of switched WANs (backbones), LANs, point-to-point WANs, and connecting or switching devices

## Slide 3: Outline
Wired Local Area Networks
Wireless LANs
Point-to-Point WANs
Switch WANs
Connecting Devices

## Slide 4: Local Area Network (LAN)
In a limited geographic area
  A department, a building, or a campus
Popular LANs
  Ethernet LANs
  Token Ring LANs
  Token Bus LANs
  FDDI
  ATM LANs

## Slide 5: IEEE Standards
IEEE Project 802
  Specify functions of the physical layer and the data link layer of major LAN protocols
Relationship of the 802 standard to OSI model
  IEEE subdivide the data link layer into two sublayers
    Logical Link Control (LLC)
    Media Access Control (MAC)

## Slide 6
Figure 3-3
IEEE Standards for LANs
The McGraw-Hill Companies, Inc., 2000

## Slide 7: Frame Format
Ethernet specifies only one frame type containing seven fields
Ethernet is an unreliable medium
  Does not provide acknowledgement mechanism

## Slide 8: Frame Format (Cont.)
Preamble
  7 bytes of alternating 1s and 0s
  Added at the physical layer for synchronization
Start frame delimiter
  1 bytes: 10101011, the last chance to synchronize
  The last 11 signals that the next field is the address
Destination address: 6 bytes
  Physical address of the intermediate or the destination station
Source address: 6 bytes
  Physical address of the sending or intermediate station

## Slide 9: Frame Format (Cont.)
Length/type: has one of two meaning
  < 1518: length: the length of the data field
    RFC 1042:
  > 1536: type: define the upper layer protocol
    RFC 894:
      0800: IP
      0806: ARP
      8035: RARP
Data: 46~1500 bytes
  Padding is needed if upper layer packet is less than 46 bytes
CRC: CRC-32 for error detection

## Slide 10: Frame Length
The Ethernet frame must have a minimum and maximum frame length

## Slide 11: Frame Length (Cont.)
Why impose the minimum frame length restriction ?
  Required for the operation of CSMA/CD
  Introduced later
Why impose the Maximum frame length restriction ?
  Memory was expensive when Ethernet was design
    Helped to reduce the size of the buffer if maximum frame length is imposed
  Prevent one station from monopolizing the shared medium

## Slide 12: Addressing
Data link address = physical address = MAC address

## Slide 13: Addressing (Cont.)
Source address is always unicast
Destination Address
  Unicast
    One single recipient
    The least significant bit of the first byte in a destination address is 0
  Multicast
    A group of recipients
    The least significant bit of the first byte in a destination address is 1
  Broadcast: a special case of multicast
    All stations connected to the LAN
    48 1s

## Slide 14: Unicast and Multicast Addresses

## Slide 15: Example 3.1
Define the type of the following destination addresses:
a. 4A:30:10:21:10:1B
b. 47:20:1B:2E:08:EE
c. FF:FF:FF:FF:FF:FF
Solution
a. This is a unicast address because A in binary is 1010 (even).
b. This is a multicast address because 7 in binary is 0111 (odd).
c. This is a broadcast address because all digits are F’s.

## Slide 16: Addressing (Cont.)
The way the addresses are sent out on the line
  The transmission is left-to-right, byte by byte
  However, for each byte, it is sent right-to left, bit by bit
Thus, the bit that defines an address as unicast or multicast arrives first at the receiver

## Slide 17: Example 3.2:
Show how the address 47:20:1B:2E:08:EE is sent out on line
Solution:
Transform to binary:
Since the address is sent left-to-right, byte-by-byte; for each byte, it is sent right-to-left, bit by bit
← 11100010 00000100 11011000 01110100 00010000 01110111
01000111:00100000:00011011:00101110:11101110

## Slide 18: Ethernet Evolution
Designed in 1973 by Xerox
Four Generations
  Standard Ethernet (10 Mbps)
  Fast Ethernet (100 Mbps)
  Gigabit Ethernet (1 Gbps)
  Ten-Gigabit Ethernet (10 Gbps)

## Slide 19: Standard Ethernet
Logical topology is a bus
  Physical topology may be a bus or a star
  The medium is shared between stations
    Only one station at a time can use it
  All stations receive a frame sent by a station
    Only destination keeps it while the rest drop it
Access Method: CSMA/CD

## Slide 20: Access Method: CSMA/CD
CSMA/CD: Carrier Sense Multiple Accesses with Collision Detection
CSMA:
  Multiple access: every station has an equal right
  Carrier sense: sense the medium before sending a frame.
    Starting transmission if not data on the medium
    “Sense before sending” or “listen before talk”
However, CSMA only reduce the possibility of collision, but it can not eliminate it.

## Slide 21
CSMA Problem
The McGraw-Hill Companies, Inc., 2000

## Slide 22: Access Method: CSMA/CD
Collision Detection
  Station must continue to listen after sending has begun (sending while listening)
  If a collision
    Send a jam signal to destroy the data
    Wait for a random time and try again
In the next slide
  t1: A sense the medium and find it idle, so sends a frame
  t2: C sense the medium and find it idle, so sends a frame
  t3: C detects a collision and abort the transmission
  t4: A detects a collision and abort the transmission

## Slide 23: Collision of the First Bit in CSMA/CD

## Slide 24: Minimum Frame Size
For CSMA/CD to work
  We need a restriction on the frame size
  The transmission time of a frame must be at least two times the maximum propagation time
    Assume that worst-case that the two stations are the maximum distance apart

## Slide 25: Example:
Assume that
  The length of a 10BASE5 cable is 2500 meters
  The data rate is 10 Mbps
  Propagation speed is 200,000,000 meters/sec
  Ignore any propagation delay in the connecting devices
Question 1: how long does it take for a bit to travel from the network distance ?
Answer:
  2500 m / 200,000,000 meters/second = 12.5 microseconds

## Slide 26: Example (Cont.):
Questions 2: find the maximum time it takes to sense a collision
Note:
  The worst case occurs when data are sent from one end and collision happens at the other end
  The signal needs to take a round-trip
Answer:
  In the worst case, the collision would be sensed in 2 × 12.5 = 25 microseconds

## Slide 27: Example (Cont.):
Questions 3: find the minimum size of a frame for collision detection to work properly
Answer:
  Assume that x equal the minimum number of bits
  X bits / 10M bits/second = 0.000025 seconds
  X = 10,000,000 × 0.000025 = 250 bits = 31.25 bytes
  The minimum frame size must be larger than 32 bytes for an Ethernet network of 2500 meters to work properly.
In fact, the minimum size is set to 512 bits to allow for propagation delay in the connecting devices.

## Slide 28: Procedure: CSMA/CD Flow Diagram

## Slide 29: Fast Ethernet
Goal
  Upgrade the data rate to 100 Mbps
  Make it compatible with Standard Ethernet
  Keep the same 48-bit address
  Keep the same frame format
  Keep the same minimum and maximum frame lengths

## Slide 30: Fast Ethernet (Cont.)
Keep the MAC sub-layer untouched
However, drop the bus and keep only star topology
Two implementation choice for star topology
  Half duplex: stations are connected via a hub
    Use CSMA/CD
  Full duplex: station are connected via a switch
    Every station is connected by two separate paths to the hub
    No collision and no need for CSMA/CD
    But keep CSMA/CD for backward compatibility

## Slide 31: Gigabit Ethernet
Goal
  Upgrade the data rate to 1 Gbps
  Make it compatible with Standard or Fast Ethernet
  Keep the same 48-bit address
  Keep the same frame format
  Keep the same minimum and maximum frame lengths
  To support auto-negotiation as defined in Fast Ethernet (Skip!)

## Slide 32: Gigabit Ethernet (Cont.)
Also two modes
  Full-Duplex Mode
    Almost all implementations of Gigabit Ethernet uses this mode
    No collision and CSMA/CD is not used
    Thus, the maximum length of the cable is determined by the signal attenuation (衰減) of the cable
      Not by the collision detection process
  Half-Duplex Mode

## Slide 33: Ten-Gigabit Ethernet
Goal
  Upgrade the data rate to 10 Gbps
  Make it compatible with Standard, Fast, and Gigabit Ethernet
  Keep the same 48-bit address
  Keep the same frame format
  Keep the same minimum and maximum frame lengths
  Allow the interconnection of existing LANs into a metropolitan area network (MAN) or a wide are network (WAN)
  Make Ethernet compatible with technologies such as Frame Relay or ATM
Implementation
  Operate only in full duplex mode

## Slide 34: Outline
Wired Local Area Networks
Wireless LANs
Point-to-Point WANs
Switch WANs
Connecting Devices

## Slide 35: IEEE 802.11 Wireless LANs
Sometimes called wireless Ethernet
Family
  IEEE 802.11: 2 Mbps
    2.40~2.48 GHz
  IEEE 802.11b: 11 Mbps
    2.40~2.48 GHz
  IEEE 802.11a: 54 Mbps
    5 GHz
  IEEE 802.11g: 54 Mbps
    2.40~2.48 GHz
  IEEE 802.11n: 300 Mbps
    2.4 or 5 GHz

## Slide 36
Figure 3-12
ISM Bands
ISM: Industrial, Scientific and Medical bands
Unlicensed band
The McGraw-Hill Companies, Inc., 2000

## Slide 37: Architecture
Basic Service Set (BSS)
  With an AP
  Without an AP: independent BSS, also called ad hoc architecture
Extended Service Set (ESS)
  Made of two or more BSSs with APs
  BSSs are connected through a distribution system
    Usually a wired LAN

## Slide 38
Figure 3-13
BSSs
The McGraw-Hill Companies, Inc., 2000

## Slide 39
Figure 3-14
Extended Service Sets (ESSs)
The McGraw-Hill Companies, Inc., 2000

## Slide 40: MAC Layer in IEEE 802.11
DCF (Distributed Coordination Function): CSMA/CA
PCF (Point Coordination Function): polling
  Option

## Slide 41: MAC Layer in IEEE 802.11 (Cont.)
Why not adopt CSMA/CD?
  For collision detection, must send data and receive collision signals at the same time
    Mean costly stations and increased bandwidth requirements
  Collisions may not be detected due to hidden station problem
  The distance between stations would be great
    Signal fading in a large distance could prevent a station at one end from hearing a collision at the other end

## Slide 42: CSMA/CA
Carrier Sense Multiple Access with Collision Avoidance: CSMA/CA
Cannot detect collision
  Need ack. packet
  However, Ethernet does not use ack. packet

## Slide 43: Frame Exchange Time Line
References the next two slides
  Sense the medium before sending a frame
    If channel is idle, wait for a DIFS period and then sends a RTS (request to send) frame
  After receiving the RTS and wait for a SIFS period
    Destination node sends a CTS (clear to send) frame
  Send the data after waiting SIFS period
  Return an ACK after waiting SIFS period

## Slide 44: CSMA/CA Flow Diagram

## Slide 45: CSMA/CA and NAV
A
l
l
o
t
h
e
r
s
t
a
t
i
o
n
s
•
•
•
S
o
u
r
c
e
D
e
s
t
i
n
a
t
i
o
n
T
i
m
e
T
i
m
e
T
i
m
e
T
i
m
e

## Slide 46: DIFS and SIFS
SIFS (Short Interframe Space): 10 us in 802.11b
DIFS (DCF Interframe Space): 50 us in 802.11b
Why? Providing Priority Access
  In the above slide
  If another station want to send frame at the SIFS period between frame 1 and frame 2
    It would find that there is no carrier and send its frame
    Cause collision when frame 2 (CTS) is sent by destination
  Thus, station must wait for DIFS
  Thus, stations waiting for SIFS period has higher priorities than stations waiting for DIFS period

## Slide 47: Network Allocation Vector
NAV: Network Allocation Vector
All of the RTS/CTS/DATA frames’ header contains a duration field.
  Indicate the amount of time the sender needs to occupy the channel
  When other stations received this frame
    Start a timer, called NAV, that equals to the duration value
  If NAV has not expired, other stations should not sense the medium and send the frame

## Slide 48: CSMA/CA: Without RTS/CTS
Ack
Data
NAV
Src
Dest
Other
Defer Access
CW
Backoff after Defer
DIFS
SIFS
DIFS

## Slide 49: CSMA/CA: With RTS/CTS
RTS
CTS
Ack
Data
NAV
Next MPDU
Src
Dest
Other
CW
Defer Access
Backoff after Defer
NAV
(RTS)
(CTS)
NAV
(Data)

## Slide 50: Fragmentation
Fragmentation
  Divide a large frame into smaller ones
Recommends fragmentation
  Since the wireless channel is very noisy
  Fragmentation is used to increase reliability
  More efficient to resend a smaller frame than a large one

## Slide 51: Fragmentation (Cont.)
Fragment Bursts which are individually acknowledged.
  Retransmission is applied to each fragment

## Slide 52: Frame Format
Frame control (FC): 2 bytes
  Define the type of the frame and some control information
D: 2 bytes
  Define the duration of the transmission
Addresses
  Four addresses with each 6 bytes
Sequence control: 2 bytes
  Define the sequence number of the frame
Frame body: 0~2312 bytes
  Contain the information based on the type and the subtype defined in the FC field
FCS: 4 bytes
  CRC-32 error detection sequence

## Slide 53: Addressing Mechanism
Address 1: always the address of the next device
Address 2: always the address of the previous device

## Slide 54
Figure 3-14
Extended Service Sets (ESSs)
The McGraw-Hill Companies, Inc., 2000

## Slide 55: Hidden and Exposed Station Problems
Hidden station problem
  Solution: RTS (Request To Send) and CTS (Clear To Send)
Exposed station problem (Skip!)
  A node is prevented from sending packets to other nodes due to a neighboring transmitter.
  Cannot be solved by RTS/CTS

## Slide 56: Hidden Station Problem

## Slide 57: Use of Handshaking to Prevent Hidden Station Problem

## Slide 58: Outline
Wired Local Area Networks
Wireless LANs
Point-to-Point WANs
Switch WANs
Connecting Devices

## Slide 59: Point-to-Point WANs
Connect two devices using a line available from a public network such as a telephone network
Physical layer
  V.90 (56K) Modem
  Digital Subscriber Line (DSL)
  Cable Modem
  T lines: T1 and T3
  SONET (Synchronous Optical Network)

## Slide 60: Point-to-Point WANs (Cont.)
Data link layer
  PPP: Point-to-Point Protocol
    A way to encapsulate IP datagrams
    A Link Control Protocol (LCP)
    A family of Network Control Protocols (NCPs) specific to different network layer protocols
  Link Control Protocol (LCP)
  Network Control Protocol (NCP)
  PPPoE

## Slide 61: Outline
Wired Local Area Networks
Wireless LANs
Point-to-Point WANs
Switch WANs
Connecting Devices

## Slide 62: Switched WANs
The backbone in the Internet are usually a switched WAN
A switched WAN is a wide area network that
  Cover a large area ( a state or a country)
  Provide access at several points to the user
    Allow the connections of several inputs and outputs

## Slide 63: Switched WANs (Cont.)
Differences between a switched WAN and LAN
  Instead of a bus or star topology, switches are used to create multiple paths between two nodes
  LAN technology is considered a connectionless but switched WAN is a connection-oriented technology
Three common switched WAN
  X.25
  Frame Relay
  ATM

## Slide 64: Outline
Wired Local Area Networks
Wireless LANs
Point-to-Point WANs
Switch WANs
Connecting Devices

## Slide 65: Connecting Devices
The Internet is a combination of LANs and WANs
  Joined by the connecting devices
Repeater and Hub: the first layer
Bridges: first two layers
Routers: first three layers
Switches
  Sophisticated bridges or sophisticated routers

## Slide 66
Connecting Devices
The McGraw-Hill Companies, Inc., 2000

## Slide 67: Repeaters
Operate only in the physical layer
Receive a signal and regenerate the original bit pattern
  Does not an amplifier
    Amplifier does not discriminate between the intended signal and noise; just amplifies equally everything fed into it
  Repeater regenerates the signal
    If a weakened or corrupted signal, create a copy at the original strength
Can extend the physical length of a network
  Connect two segments of the same LAN
  The whole network is still one LAN

## Slide 68
Figure 3-27
Repeater
The McGraw-Hill Companies, Inc., 2000

## Slide 69: Function of a Repeater

## Slide 70: Hubs
Operate only in the physical layer
A multi-port repeater
Create connections in a physical star topology
  The whole network is still one single LAN
  Packets sent by a station are received by every other station

## Slide 71
Figure 3-28
Hubs
The McGraw-Hill Companies, Inc., 2000

## Slide 72
A repeater or hub forwards every bit; it has no filtering capability.
Note

## Slide 73: Bridges
Operate in both the physical and the data link layer
  Physical layer: regenerate the signal it receives
  Data link layer: check the physical address
Has no physical address
  Act only as a filter
All the segments connected by a bridge are still part of one LAN

## Slide 74: Filtering Example
A LAN is divided into two segments separated by a bridge
If a packet destined for 712B13456142 arrives at port 1
  Consult its table to find the departing interface

## Slide 75
Bridge
The McGraw-Hill Companies, Inc., 2000

## Slide 76: Transparent Bridges
Stations are completely unaware of its existence
  If a bridge is added or deleted, reconfiguration of the stations is unnecessary
Criteria for a system equipped with a transparent bridge
  Frames must be forwarded from one station to another
  The forwarding table is automatically made by learning frame movement in the network
  Loops in the system must be prevented
Also called a learning bridge
Learning: create the table mapping from the packets it receives
  Source address and the arriving interface

## Slide 77: Example: Learning Bridge
When station A sends a frame to station D
  The bridge does not have an entry
    The frame goes out from all three ports
  From the source address and the incoming port
    A must be connected to port 1
When station D sends a frame to station B
  Flood the network again
  Create the second entry for D
The learning process continues

## Slide 78: Example 1: Learning Bridge
M
M
M
M

## Slide 79
A bridge has a table used in filtering decisions.
Note
A bridge does not change the physical (MAC) addresses in a frame.

## Slide 80: Routers
A router is a three-layer devices
  Physical layer: regenerate the signal it receives
  Data link layer: check the physical address (source and destination) in the packet
  Network: check the network address
A router is a internetworking device
  Connect independent networks (LANs or WANs) to from an internetwork or an internet

## Slide 81: Routers (Cont.)
Differences between a router and a repeater or a bridge
  A router has a physical and IP address for each of its interfaces
    Routers have addresses on two or more networks
  A router acts only on those packets whose destination physical address matches the physical address of the incoming interface
  A router changes the physical address of the packet when it forward the packet

## Slide 82
Figure 3-30
Routing Example
The McGraw-Hill Companies, Inc., 2000

## Slide 83: Switches
Two different meaning
  Two-layer switch
    A bridge with many interface and a design that allow better performance
  Three-layer switch
    A router with an improved design to allow better performance