## Slide 1: Chapter 4 Introduction to Network Layer

## Slide 2: Outline
Introduction
Switching
Packet Switching at Network Layer
Network Layer Services
Other Network Layer Issues

## Slide 3
Introduction
4.1
The McGraw-Hill Companies, Inc., 2000

## Slide 4: Internet as a Combination of LANs and WANs Connected Together
Switching occurs at each connecting device

## Slide 5
Switching
4.2
The McGraw-Hill Companies, Inc., 2000

## Slide 6: Local Area Network (LAN)
Switching
  Connect one port to another port
Two methods
  Circuit switching
  Packet switching

## Slide 7: Circuit Switching
Before the delivery of the message, a physical circuit is established between the source and destination
After the circuit is established
  The entire message is transformed following this circuit
Example
  Telephone systems

## Slide 8: Packet Switching
A message from the upper layer is divided into packets and each packet is sent through the network
The network layer in Internet is a packet-switched network
In packet switching, two approaches to route the packets to the destination
  The datagram approach: connectionless service
  The virtual circuit approach: connection-oriented service

## Slide 9
Packet Switching At
Network Layer
4.3
The McGraw-Hill Companies, Inc., 2000

## Slide 10: Connectionless Service
The network layer in Internet adopt connectionless service
Why? Simple
Each packet is treated independently
  Each packet has no relationship to any other packet belonging to the same message
  The packet in a message may or may not travel the same path to destination
The router routes the packet based only on the destination network address

## Slide 11: A Connectionless Packet-Switched Network

## Slide 12: Forwarding Process in a Connectionless Network

## Slide 13: Delay in a Connectionless Network

## Slide 14: Connection-Oriented Service (Skip!)
There is a relation between all packets belonging to a message
Before all datagrams in a message can be sent
  A virtual connection must be setup
  All datagrams follows the same path
In addition to source and destination addresses
  Each packet must contain a flow label, or a virtual circuit identifier that defines the virtual path the packet should follow

## Slide 15: A Connection-Oriented Packet Switched Network (Skip!)

## Slide 16: Connection-Oriented Service (Cont.) (Skip!)
Each packet is forwarded based on the label in the packet
Thus, why needs source and destination addresses?
  Part of the path may still be using the connectionless service
  The protocol at the network layer is designed with these addresses
    It may take a while before they can be changed
Three-phase process is used to create a connection-oriented service
  Setup, data transfer, and teardown

## Slide 17: Forwarding Process in a Connection-oriented Network (Skip!)

## Slide 18: Connection-Oriented Service: Setup Phase (Skip!)
Router creates an entry for a virtual circuit
Two auxiliary packets need to be exchanged: request packet and acknowledgment packet
Request packet (ref. the next slide)
  A sends a request packet to B
  R1 receives the packet.
    Assume that the outgoing port is 3 (How to derive is shown in the future)
    Create an entry in its table
      Incoming port = 1,
      Chooses an available incoming label = 14
      Outgoing port = 3
    R3 and R4 do the same work
    B receives the request packet and assign a label = 77

## Slide 19: Sending Request Packet in a Virtual-Circuit Network (Skip!)

## Slide 20: Connection-Oriented Service: Setup Phase (Cont.) (Skip!)
Acknowledgement packet (ref. the next slide)
  Destination sends an acknowledgement to R4
    Add the label 77 into the outgoing label
  R4 sends the acknowledgement to R3
    Contain the incoming table 22
  R3 and R1 perform the same work
  A uses label 14 as the outgoing label to send data to B

## Slide 21: Setup Acknowledgement in a Virtual-Circuit Network (Skip!)

## Slide 22: Connection-Oriented Service: Data Transfer Phase (Skip!)
Data Transfer (ref. the next slide)
  A uses label 14 to send packets
  R1 changes the label to 66 and send to R3
  R3 changes the label to 22 and send to R4
  R4 changes the label to 77 and send to B
All packets in the message from the same sequence of labels and arrive in order at the destination

## Slide 23: Flow of One Packet in an Established Virtual Circuit (Skip!)

## Slide 24: Connection-Oriented Service: Tear Down Phase (Skip!)
Tear Down
  A sends a special packet, called teardown packet
  B responds with a confirmation packet
  Then all routers delete the corresponding entry from their tables

## Slide 25: Delay in a Connection-Oriented Network (Skip!)

## Slide 26
Network Layer Services
4.4
The McGraw-Hill Companies, Inc., 2000

## Slide 27: Network Layer Services
Logical addresses
Services provided at the source computer
Services provided at each router
Services provided at the destination computer

## Slide 28: Logical addresses
Since network layer provide end-to-end communication
  Two ends needs a universal identification system
  Network-layer address or logical address

## Slide 29: Services Provided at the Source Computer
Packetizing
  Encapsulate the data from upper layer into a datagram by adding a header
Find the logical address of the next hop
  Usually, the datagram may pass through many network
  Need to consult a routing table to find the logical address of the next hop
Finding the physical (MAC) address of the next hop
  The delivery is actually perform at the data link layer
    Need MAC address to do the delivery
  Need to map the next-hop logical address to the MAC address
Fragmenting datagram if necessary
  Most LAN and WAN has a MTU (maximum transfer unit) limit
  Fragment is needed if the datagram is larger than the MTU

## Slide 30: Services Provided at the Source Computer

## Slide 31: Services Provided at Each Router
First, check the validity of the datagram using the checksum
Then, provides three services the same as the last three processes mentioned for a source
  Find the logical address of the next hop
  Finding the physical (MAC) address of the next hop
  Fragmenting datagram if necessary

## Slide 32: Processing at Each Router

## Slide 33: Services Provided at the Destination Computer
De-packetize
  Extract the data from each fragment
Assemble
  Assemble the fragments

## Slide 34: Processing at the Destination Computer

## Slide 35
Other Network Layer
Issues
4.5
The McGraw-Hill Companies, Inc., 2000

## Slide 36: Other Network Issues
Error control
Flow control
Congestion control
Quality of service
Routing
Security

## Slide 37: Other Network Issues: Error Control
Error control:
  Detect corrupted, lost, or duplicated datagrams
  Correct errors after they have been detected
Questions:
  Hop-to-hop error control is already implement at the data link layer
  Why doe we need end-to-end error control at the network layer
Answers (ref. the next slide)
  The data link layer can miss any error that occurs when the datagram is being processed by the router

## Slide 38: Error Checking at the Data Link Layer

## Slide 39: Other Network Issues: Error Control (Cont.)
However, designers of the network layer wanted to make this layer simple and fast
  If more rigorous error checking is needed, done at the upper layers
Thus, only checksum is used
  But only apply to the header

## Slide 40: Other Network Issues: Flow Control
Flow control
  Regulate the amount of data a source can send without overwhelming the receiver
But, no flow control is used in network layer. Why?
  Receiver may rarely be overwhelmed
    Since the job of network layer at receiver is so simple
      Does not need to perform error control in network layer
  Upper layer can implement buffers
  Flow control can be provided at upper layer protocol

## Slide 41
No flow control is provided for the current version of Internet network layer.
Note

## Slide 42: Other Network Issues: Congestion Control
Congestion
  The number of datagrams are beyond the capacity of the network or routers
  Some routers may drop some of the datagrams
Congestion control
  Congestion control in a connectionless network
  Congestion control in a connection-oriented network

## Slide 43: Congestion Control in a Connectionless Network
Solutions:
  Signaling
    Set a bit in the datagram to inform the source
    No used in the network layer
  Choke packet:
    A special packet can be sent from a router to the sender to inform the congestion
    Adopted by ICMP
  Ranking
    Rank the packets by their importance in the whole message
    Drops packets that are less important when congested

## Slide 44: Congestion Control in a Connection-Oriented Network (Skip!)
Two Methods:
  Creates an extra virtual circuit when there is a congestion
  Advanced Negotiation
    A level of traffic is negotiated and granted if feasible when the virtual circuit is setup
    Better solution

## Slide 45: Other Network Issues (Cont.)
Quality of Service
  For multimedia communication
Routing
  How to create routing table or a virtual circuit
  By routing protocols
    Make routing table, maintain them, and update them
Security
  IPSec