## Slide 1: Chapter 6 Delivery and Routing of IP Packets

## Slide 2: Outline
Delivery
Forwarding
Structure of a Router

## Slide 3: Delivery v.s. Routing
Delivery
  The way a packet is handled by the underlying networks under the control of the network layer
    Direct v.s. indirect delivery
Forwarding
  The way a packet is delivered to the next station
    Forwarding based on destination address
    Forwarding based on the label

## Slide 4
Delivery
6.1
The McGraw-Hill Companies, Inc., 2000

## Slide 5: Delivery
Delivery of a packet
  The network layer supervises the handling of the packet by the underlying physical networks
Two method
  Direct versus indirect delivery

## Slide 6: Direct Delivery
The final destination is a host in the same physical network as the deliverer
  When the source and destination are located on the same physical network
  Or the delivery is between the last router and the destination host

## Slide 7
Figure 6-1
Direct Delivery
The McGraw-Hill Companies, Inc., 2000

## Slide 8: Direct Delivery (Cont.)
How to determine if the delivery is direct
  Compare the network addresses between the destination and the current network
For direct delivery, the sender uses the destination IP address to find the destination physical address
  Static method: finding a table
  Dynamic method: use the address resolution protocol (ARP)

## Slide 9: Indirect Delivery
The destination host and the deliverer are not on the same network
  Packet goes from routers to routers
For indirect delivery
  The sender uses the destination IP address and a routing table to find the next router’s IP address
  Then, the sender uses ARP protocol to find the next router’s physical address

## Slide 10
Figure 6-2
Indirect Delivery
The McGraw-Hill Companies, Inc., 2000

## Slide 11: Indirect Delivery (Cont.)
A delivery always involves one direct delivery but zero or more indirect deliveries
Besides, the last delivery is always a direct delivery

## Slide 12
Forwarding
6.2
The McGraw-Hill Companies, Inc., 2000

## Slide 13: Forwarding
Forwarding: place the packet in its route to its destination
Two methods
  If IP is a connectionless protocol,
    Forwarding is based on the destination addresses of the IP datagram
  If IP is a connection-oriented protocol
    Forwarding is based on the label attached to an IP datagram

## Slide 14: Forwarding Based on Destination Address
Forwarding requires a host/router to have a routing table
However, with the increase of hosts,
  The number of entries in the routing table also increase
Techniques to decrease the routing table size and handle issues such as security
  Next-hop routing
  Network-specific routing
  Host-specific routing
  Default routing

## Slide 15: Next-Hop Routing
Routing table holds only the address of the next hop
  Instead of holding information about the complete route

## Slide 16
Figure 6-3
Next-Hop Routing
The McGraw-Hill Companies, Inc., 2000

## Slide 17: Network-Specific Routing
Use only one entry to define the address of the network itself, i.e., network address
  Instead of having an entry for every host connected to the same physical network

## Slide 18
Figure 6-4
Network-Specific Routing
The McGraw-Hill Companies, Inc., 2000

## Slide 19: Host-Specific Routing
The destination host address is given in the routing table
The inverse of network-specific routing
Not efficient for performance
  But, in some occasions, the administrator wants to have more control over routing
    Checking the route
    Providing security

## Slide 20
Figure 6-5
Host-Specific Routing
The McGraw-Hill Companies, Inc., 2000
R1
Assume that the path from R3
to B is insecure

## Slide 21: Default Routing
Instead of listing all networks in the routing table
  Just use one entry called default
  Network address is 0.0.0.0

## Slide 22
Figure 6-6
Default Routing
The McGraw-Hill Companies, Inc., 2000

## Slide 23: Forwarding Classification
Forwarding with Classful Addressing
  Forwarding without subnetting
  Forwarding with subnetting
Forwarding with Classless Addressing

## Slide 24: Forwarding without Subnetting
The existence of a default mask in a classful address makes for forwarding process simple
Most routers in classful addressing are not involved in subnetting
  Since subnetting happens inside an organization
A forwarding module would consists of three tables
  One for each unicast class
  If support multicast, add one more table to handle class D addresses

## Slide 25: Forwarding without Subnetting
Each routing table has a minimum of three columns
  Network address of the destination network
    Assume use the network-specific forwarding, not the host-specific forwarding
  Next-hop address
    Tell which router the packet must be delivered for an indirect delivery
    Empty for a direct delivery
  Interface number
    Define the outgoing port from which the packet is sent out

## Slide 26: Simplified Forwarding Module in Classful Address without Subnetting

## Slide 27: Steps of Forwarding without Subnetting
Extract the destination address of the packet
Make a copy of the destination address and find the class of its address
  Shift the copy of the address 28 bits to the right
  The result is a 4-bit number used to determine the class
Use the result in steps 2 to extract the network address
  By masking off the rightmost 8, 16, or 24 bits since we have the mask now
The class of the address and the network address are used to find out next-hop information
  The class determines the table to be searched
  Then search the table for the network address
    If found, use the next-hop address and the interface number; else, use the default route
Use the ARP module to find the physical address of the next router
  By the next-hop address and the interface number

## Slide 28: Example 6.1
Show the routing table for router R1

## Slide 29: Example 6.1: Solution
Following figure shows the three tables used by router R1.
Some entries in the next-hop address column are empty
  Because the destination is in the same network to which the router is connected (direct delivery).
  Thus, the next-hop address used by ARP is simply the destination address of the packet

## Slide 30: Table for Example 1

## Slide 31: Example 6.2
Router R1 in above figure receives a packet with destination address 192.16.7.14. Show how the packet is forwarded
Solution
  The destination address is 11000000 00010000 00000111 00001110.
  A copy of the address is shifted 28 bits to the right. The result is 00000000 00000000 00000000 00001100 or 12.
    The destination network is class C.
  The network address is extracted by masking off the leftmost 24 bits of the destination address; the result is 192.16.7.0.
  The table for Class C is searched and the network address is found in the first row.
  The next-hop address 111.15.17.32. and the interface m0 are passed to ARP

## Slide 32: Example 6.3
Router R1 in above figure receives a packet with destination address 167.24.160.5. Show how the packet is forwarded.
Solution
  The destination address is 10100111 00011000 10100000 00000101.
  A copy of the address is shifted 28 bits to the right. The result is 00000000 00000000 00000000 00001010 or 10.
    The class is B.
  The network address is 167.24.0.0.
  The table for Class B is searched.
    No matching network address is found.
    The packet needs to be forwarded to the default router (the network is somewhere else in the Internet).
  The next-hop address 111.30.31.18 and the interface number m0 are passed to ARP.

## Slide 33: Forwarding Classification
Forwarding with Classful Addressing
  Forwarding without subnetting
  Forwarding with subnetting
Forwarding with Classless Addressing

## Slide 34: Forwarding with Subnetting
In classful addressing, subnetting happens inside an organization
The routers that handle subnetting
  At the border of the organization site
  Inside the site boundary
Number of routing tables
  If variable-length subnetting is used
    We need several tables
  Otherwise, only one is enough
    P. 112 and 115 in Chapter 5

## Slide 35: Simplified Forwarding Module in Classful Address with Subnetting

## Slide 36: Steps in Forwarding with Subnetting
Extract the destination address of the packet
Extract the subnet address by the destination address and the subnet mask (p. 72 in chapter 5)
Search the table by the subnet address to find the next-hop address and the interface number
  If no mach, use the default route
Pass the next-hop address and the interface number to the ARP

## Slide 37: Example 6.4
Following figure 6.11 shows a router connected to four subnets
Note
  The router is configured to apply the mask /18 to any destination address

## Slide 38: Figure 6.11 Configuration for Example 4

## Slide 39: Example 6.5
The router in above figure receives a packet with destination address 145.14.32.78. Show how the packet is forwarded
Solution
  The mask is /18.
  After applying the mask, the subnet address is 145.14.0.0.
  The packet is delivered to ARP with the next-hop address 145.14.32.78 and the outgoing interface m0

## Slide 40: Example 6.6
A host in network 145.14.0.0 in above figure has a packet to send to the host with address 7.22.67.91. Show how the packet is routed
Solution
  The router receives the packet and applies the mask (/18).
    The subnetwork address is 7.22.64.0.
  The table is searched and the address is not found.
    The router uses the address of the default router (not shown in figure) and sends the packet to that router

## Slide 41: Forwarding Classification
Forwarding with Classful Addressing
  Forwarding without subnetting
  Forwarding with subnetting
Forwarding with Classless Addressing

## Slide 42: Forwarding with Classless Addressing
In classless addressing,
  Cannot derive the network address from the destination address in the packet
Solution
  Include the mask (/n) of the corresponding block in the table
  Thus, a classless routing table needs at least four columns

## Slide 43: Simplified Forwarding Module in Classless Address

## Slide 44: Example 6.7
Make a routing table for router R1 using the configuration in Figure 6.13
Solution:

## Slide 45: Configuration for Example 7

## Slide 46: Example 6.8
Show the forwarding process if a packet arrives at R1 in above figure with the destination address 180.70.65.140
Solution: the router performs the following steps:
  The first mask (/26) is applied to the destination address.
    The result is 180.70.65.128, which does not match the corresponding network address
  The second mask (/25) is applied to the destination address.
    The result is 180.70.65.128, which matches the corresponding network address.
    The next-hop address (the destination address of the packet in this case) and the interface number m0 are passed to ARP for further processing

## Slide 47: Example 6.9
Show the forwarding process if a packet arrives at R1 in above figure with the destination address 201.4.22.35
Solution: the router performs the following steps
  The first mask (/26) is applied to the destination address.
    The result is 201.4.22.0 => (X).
  The second mask (/25) is applied to the destination address.
    The result is 201.4.22.0 => (X).
  The third mask (/24) is applied to the destination address.
    The result is 201.4.22.0 => (0)
    The destination address of the package and the interface number m3 are passed to ARP

## Slide 48: Example 6.10
Show the forwarding process if a packet arrives at R1 in above figure with the destination address 18.24.32.78
Solution
  This time all masks are applied to the destination address, but no matching network address is found.
  When it reaches the end of the table, the module gives the next-hop address 180.70.65.200 and interface number m2 to ARP.
  This is probably an outgoing package that needs to be sent via the default router, to some place else in the Internet

## Slide 49: Example 6.11
The routing table for router R1 is given in Table 6.2. Can we draw its topology?

## Slide 50: Example 11: Solution
We know some facts but we don’t have all for a definite topology.
Router R1 has three interfaces: m0, m1, and m2.
There are three networks directly connected to router
  110.70.0.0/16, 180.14.0.0/16, 190.17.0.0/16
There are two networks indirectly connected to R1
  140.6.12.64/26 and 130.4.8.0/24
There must be at least three other routers involved
  From the next-hop column

## Slide 51: Example 11: Solution (Cont.)
One router, the default router, is connected to the rest of the Internet.
However,
  We do not know if network 130.4.8.0 and 140.6.12.64 is directly connected to router R2 and R3 or through a point-to-point network (WAN) and another router.
Figure 6.14 shows our guessed topology

## Slide 52: Guessed topology for Example 6

## Slide 53: Address Aggregation
In classless address
  The number of entries will increase
    Since classless addressing is to divide up the whole address space into blocks
Problem:
  Vast routing table and increased overhead to search table

## Slide 54: Address Aggregation (Cont.)
Solutions: address aggregation
In the following figure
  R1 has a longer routing table
    Connect four organization
  R2 has a small routing table
    Any packet with destination 140.24.7.0~140.24.7.255 is sent out from interface m0
      Regardless of the organization number
    Called address aggregation
      The blocks of addresses for four organization are aggregated into one large block
      We do not have to specify each organization with an entry

## Slide 55: Address Aggregation

## Slide 56: Longest Mask Matching
However, if organization 4 is not geographically close to the other three networks
  Can we still use the address aggregation and assign 140.24.7.192/26 to organization 4?
Ans: Yes
  Since routing in classless addressing uses longest mask matching
Longest mask matching
  Routing table is sorted from the longest mask to the shortest mask
  If there are three masks, /27, /26, /24
    /27 is the first entry and /24 is the last one

## Slide 57: Longest Mask Matching (Cont.)
Example, in the following figure
  Organization 4 is moved
  If an packet with destination address 140.24.7.200 is arrived at R2
    The first mask at router R2 is applied => match
    Route from interface m1 and reach organization 4
  If not use longest mask matching
    Apply the /24 mask would result in the incorrect routing
Thus
  We can still aggregate organization 1~3 into a large block while still assign 140.24.7.192/26 to organization 4

## Slide 58: Longest Mask Matching (Cont.)

## Slide 59: Hierarchical Routing
To further reduce the size of routing table
  Create a sense of hierarchy in the Internet architecture and routing tables
Internet is divided into international and national ISP
  National ISP are divided into regional ISPs
  Regional ISP are divided into local ISPs
If a local ISP divide its block (a.b.c.d/n) into smaller blocks
  However, to the rest of the Internet, routers do not know such a division
  Thus, all customers of the local ISP are still defined as a.b.c.d/n to the rest of Internet

## Slide 60: Example 12
Consider the following figure
  A regional ISP is granted 16384 addresses starting from 120.14.64.0/18
  The regional ISP has decided to divide this block into four subblocks, each with 4096 addresses.
  Three of these subblocks are assigned to three local ISPs,
  The second subblock is reserved for future use

## Slide 61: Hierarchical Routing with ISPs

## Slide 62: Example 12 (Cont.)
The first local ISP has divided its assigned subblock into 8 smaller blocks
  Assigned each to a small ISP.
  Each small ISP provides services to 128 households (H001 to H128), each using four addresses.
The second local ISP has divided its block into 4 blocks
  Assigned the addresses to 4 large organizations (LOrg01 to LOrg04).
The third local ISP has divided its block into 16 blocks
  Assigned each block to a small organization (SOrg01 to SOrg15).

## Slide 63: Example 12 (Cont.)
There is a sense of hierarchy in this configuration.
  All routers in the Internet send a packet with destination address 120.14.64.0 to 120.14.127.255 to the regional ISP.
  The regional ISP sends every packet with destination address 120.14.64.0 to 120.14.79.255 to Local ISP1.
  Local ISP1 sends every packet with destination address 120.14.64.0 to 120.14.64.3 to H001.

## Slide 64: Geographical Routing
To decrease the size of the routing table even further
  Extend hierarchical routing to include geographical routing
Divide the entire address space into a few large blocks
  A block to North America
  A block to Europe
  A block to Asia
  A block to Africa
The routers of ISP outside of Europe have only one entry for packets to Europe in their routing table

## Slide 65: Routing Table Search Algorithm
The algorithms used in searching routing tables in classful addressing must be changed for classless addressing
The algorithm used for updating routing tables in classful addressing must be changed for classless addressing
  Mentioned in Chapter 14

## Slide 66: Searching in Classful Addressing
The routing table in classful addressing is organized as a list
However, to make search easier, the routing table can be divided into three buckets (areas)
  One for each class

## Slide 67: Searching in Classless Addressing
In classless routing, we can also use buckets
  However, 32 buckets are used instead of three
    Each buckets corresponding to each prefix length
  When a packet arrives, try the longest prefix (/32), then the next prefix (/31) and so on until matched
    Longest prefix match
However, this search method would also take quite a long time
  Use other data structures such as tree or binary tree

## Slide 68: Prefix Lengths
Classful addressing is a special case of classless addressing.

## Slide 69: Forwarding Based on Label (Skip in the Next Semester!)
In a connectionless network (datagram approach)
  Forward packets based on destination address
  Need to search the contents of a routing table
In a connection-oriented network (virtual-circuit approach)
  Forward packets based on label
  Accessing a table using an index
Routing involves searching; switching involves accessing

## Slide 70
Figure 6.18 shows a simple example of searching in a routing table using the longest match algorithm. When the forwarding algorithm gets the destination address of the packet, it needs to delve (探究) into the mask column. For each entry, it needs to apply the mask to find the destination network address. It then needs to check the network addresses in the table until it finds the match. The router then extracts the next hop address and the interface number to be delivered to the ARP protocol for delivery of the packet to the next hop.
Example 6.13

## Slide 71
Figure 6.18 Example 6.13: Forwarding based on destination address

## Slide 72
Figure 6.19 shows a simple example of using a label to access a switching table. Since the labels are used as the index to the table, finding the information in the table is immediate.
Example 6.14 (Skip In Next Semester!)

## Slide 73
Figure 6.19 Example 6.14: Forwarding based on label
Notes: interface and
label address interface and
label address 0012

## Slide 74
STRUCTURE OF
A ROUTER
6.3
The McGraw-Hill Companies, Inc., 2000

## Slide 75: Router Components
A router has four components
  Input port
  Output port
  Routing processor
  Switching fabric

## Slide 76: Input Port
Perform the physical and data link layer functions
  Bits are constructed from the received signal
  Packet is decapsulated from the frame
  Errors are detected and corrected if possible
  Buffered in queues before packets are directed to switching fabric

## Slide 77: Output Ports
Perform the same functions as the input port, but in the reverse order
  First, the outgoing packets are queued
  Then the packet is encapsulated in a frame
  Finally, the physical and MAC layer functions are applied to send the frame

## Slide 78: Routing Processor
Perform the functions of the network layer
Perform table lookup
  Search routing table to find the address of the next hop and the output port number

## Slide 79: Switching Fabrics
Most difficult task in a router
  Move the packet from the input queue to the output queue
  The speed affects
    The size of the input/output queue
    The overall delay in packet delivery
Solution: switch fabrics
Some of the fabrics
  Crossbar Switch
  Banyan Switch
  Batcher-Banyan Switch

## Slide 80: Crossbar Switch
Connect n inputs to n output in a grid
Each crosspoint has a electronic microswitch

## Slide 81: Banyan Switch
A multistage switch
  A microswitches at each stage that route packets based on the output port represented as a binary string
  For n input and n output, we have log2(n) stages
    At each stage, we need n/2 microswitches
    See the following figure
      The number of stages is log2(8) = 3
  The first stage routes packets based on the highest bit of the binary string, and so on
  Elegant design that every input port can connect to any one output port

## Slide 82: A Banyan Switch

## Slide 83: Banyan Switch (Cont.)
In the next slide
  A packet has arrived at input port 1 and go to output port 6 (110 in binary)
  First microswtich (A-2) routes the packet based on the first bit (1)
  Second microswtich (B-4) routes the packet based on the second bit (1)
  Third microswtich (C-4) routes the packet based on the third bit (0)

## Slide 84: Examples of Routing in a Banyan Switch

## Slide 85: Batcher-Banyan Switch
Problem with the banyan switch
  The possibility of internal collisions even when two packets are not heading for the same output port
One solutions: Batcher-Banyan Switch
  Sort the incoming packets according to their final destination

## Slide 86: Batcher-Banyan Switch (Cont.)
Batch-Banyan Switch
  A combination of batcher switch and banyan switch
  A trap is added between batcher switch and banyan switch
    Prevent packets with the same output destination from passing the banyan switch simultaneously
    Only one packet for each destination is allowed at each tick

## Slide 87: Batcher-Banyan Switch