## Slide 1: Chapter 7 Internet Protocol Version4 (IPv4)

## Slide 2: Outline
Introduction
Datagram
Fragmentation
Options
Checksum
IP over ATM
Security
IP package

## Slide 3
Figure 8-1
Position of IP in TCP/IP Protocol Suite
The McGraw-Hill Companies, Inc., 2000

## Slide 4: IP: Internet Protocol
An unreliable and connectionless datagram protocol
A best-effort delivery service

## Slide 5: Outline
Introduction
Datagram
Fragmentation
Options
Checksum
IP over ATM
Security
IP package

## Slide 6: Datagram
Datagrams
  Packets in the IP layers are called in datagrams
  A variable-length packet
  Consist of two parts
    Header
    Data

## Slide 7
Figure 8-2
IP Datagram
The McGraw-Hill Companies, Inc., 2000

## Slide 8: IP Datagram
Version (VER)
Header length (HLEN)
  Length of the datagram header in 4-byte words
  The length of the header is variable
    20-60 bytes
  If no options, header length is 20 bytes
    HLEN = 5

## Slide 9: IP Datagram (Cont.)
Service Type
  In the original TCP/IP, this field was referred to as type of service (TOS)
  IETF has recently changed the interpretation and name of this field, called differentiated services
  See the following slides

## Slide 10
Figure 8-3
Type of Service v.s. Service Type
The McGraw-Hill Companies, Inc., 2000
Type of Service
Differentiated Services

## Slide 11: Type of Service
Precedence
  3-bit subfield defines the priority of the datagram in issues such as congestion
    Datagrams with lowest precedence are discarded first
  However, this subfield is not used in version 4
TOS (Type of Service) bits
  4-bit subfield with each bit having a special meaning
  However, one and only one of the bits can be set

## Slide 12: Types of Services
TOS Bits | Description
0000 | Normal (default)
0001 | Minimize cost
0010 | Maximize reliability
0100 | Maximize throughput
1000 | Minimize delay

## Slide 13: Default Types of Service
Protocol | TOS Bits | Description
ICMP | 0000 | Normal
BOOTP | 0000 | Normal
NNTP | 0001 | Minimize cost
IGP | 0010 | Maximize reliability
SNMP | 0010 | Maximize reliability
TELNET | 1000 | Minimize delay
FTP (data) | 0100 | Maximize throughput
FTP (control) | 1000 | Minimize delay
TFTP | 1000 | Minimize delay
SMTP (command) | 1000 | Minimize delay
SMTP (data) | 0100 | Maximize throughput
DNS (UDP query) | 1000 | Minimize delay
DNS (TCP query) | 0000 | Normal
DNS (zone) | 0100 | Maximize throughput

## Slide 14: Default Types of Service (Cont.)
Minimum delay
  Interactive activities
  Activities requiring immediate attention
  Activities requiring immediate response
Maximum throughput
  Send bulk data
Maximum reliability
  Management activities
Minimum monetary cost
  Background activities, like Usenet News (NNTP)

## Slide 15: Differentiated Services
The first 6 bits make up the codepoint
The last two bits are not used
The 3 right-most bits are 0s
  The 3 left-most bits are interpreted the same as the precedence bits in the Service Type
The 3 right-most bits are not all 0s
  The 6 bits define 64 services based on the priority assignment by the Internet or local authorities

## Slide 16
Service Type

## Slide 17: Values for Codepoints

## Slide 18
Figure 8-2
IP Datagram
The McGraw-Hill Companies, Inc., 2000

## Slide 19: IP Datagram (Cont.)
Total length
  The total length (header plus data) of the IP datagram in bytes
  Length of data = total length – header length
Identification
  Used in fragmentation
Flags
  Used in fragmentation
Fragmentation offset
  Used in fragmentation

## Slide 20
Figure 8-4
The McGraw-Hill Companies, Inc., 2000
Why we need the total length field
  Layer 2 just drop the header and trailer
  The remaining is the datagram (length)
However, in some cases, padding is occurred
  Ethernet’s minimum frame data length is 46 bytes
  If size of the IP datagram is less than 46, some padding will be added
  Thus, check the total length field to determine how much is really data
Encapsulation of a Small Datagram in an Ethernet Frame

## Slide 21: Encapsulation of a Small Datagram in an Ethernet Frame (Cont.)

## Slide 22: IP Datagram (Cont.)
Time to live (TTL)
  Defined the maximum number of hops visited by the datagram
  When sending a IP datagram, source stores a value in TTL
    Linux 2.4 kernel set this value to 255 (maximum value)
    Windows XP set to128
  When a router receives the datagarm
    Decrement this number by one
    After being decremented, if TTL == 0, discard this datagram
  Why?
    Routing table can become corrupted and datagram may loop in the Internet
    Intentionally limit the journey of the packet
Protocol
  Define the higher-level protocol that uses the services of the IP layer
  Help in the demulplexing proccess

## Slide 23: Protocols
Value | Protocol
1 | ICMP
2 | IGMP
6 | TCP
17 | UDP
89 | OSPF

## Slide 24
Figure 8-5
DeMultiplexing
The McGraw-Hill Companies, Inc., 2000

## Slide 25: IP Datagram (Cont.)
Checksum
Source address
  Define the IP address of the source
  Never changed between the trip
Destination address
  Define the IP address of the destination
  Never changed between the trip

## Slide 26
Figure 8-2
IP Datagram
The McGraw-Hill Companies, Inc., 2000

## Slide 27
Example 7.1
An IP packet has arrived with the first 8 bits as shown:
 01000010
The receiver discards the packet. Why?
The McGraw-Hill Companies, Inc., 2000

## Slide 28
There is an error in this packet
The 4 left-most bits (0100) show the version
  which is correct
The next 4 bits (0010) show the header length
  which means (2  4 = 8), which is wrong
  The minimum number of bytes in the header must be 20
  The packet has been corrupted in transmission
Solution

## Slide 29
Example 7.2
In an IP packet, the value of HLEN is 1000 in binary. How many bytes of options are being carried by this packet?
The McGraw-Hill Companies, Inc., 2000

## Slide 30
The HLEN value is 8
  The total number of bytes in the header is 8  4 or 32 bytes
The first 20 bytes are the main header
The next 12 bytes are the options.
Solution

## Slide 31
Example 7.3
In an IP packet, the value of HLEN is 516 and the value of the total length field is 002816. How many bytes of data are being carried by this packet?
The McGraw-Hill Companies, Inc., 2000

## Slide 32
The HLEN value is 5
  the total number of bytes in the header is 5  4 or 20 bytes (no options)
The total length is 40 bytes
The packet is carrying 20 bytes of data (40-20)
Solution

## Slide 33
Example 7.4
An IP packet has arrived with the first few hexadecimal digits as shown below:
 45000028000100000102...................
How many hops can this packet travel before being dropped? The data belong to what upper layer protocol?
The McGraw-Hill Companies, Inc., 2000

## Slide 34
To find the time-to-live field, we should skip 8 bytes (16 hexadecimal digits)
The time-to-live field is the ninth byte
  Which is 01
The packet can travel only one hop
The protocol field is the next byte (02)
  The upper layer protocol is IGMP
Solution

## Slide 35: Outline
Introduction
Datagram
Fragmentation
Options
Checksum
IP over ATM
Security
IP package

## Slide 36: Maximum Transfer Unit (MTU)
Each data link layer protocol has its own frame format
  One of this field defines the maximum size of the data field
The maximum length of the IP datagram
  65,536 bytes
Fragmentation
  We must divide the IP datagram to make it possible to pass through the underlying network

## Slide 37
Figure 8-6
MTU
The McGraw-Hill Companies, Inc., 2000

## Slide 38: MTUs for Different Networks
Protocol | MTU
Hyperchannel | 65,535
Token Ring (16 Mbps) | 17, 914
Token Ring (4 Mbps) | 4, 464
FDDI | 4, 352
Ethernet | 1, 500
X.25 | 576
PPP | 296

## Slide 39: Fragmentation
When a IP datagram is fragmented
  Each fragment has its own IP header
  Most of the fields repeated but some changed
A fragmented datagram may itself be fragmented
  A datagram can be fragmented several times

## Slide 40: Fragmentation (Cont.)
A datagram can be fragmented by the source host or any router in the path
However, the reassembly is done only by the destination host
  Each fragment becomes an independent datagram, and thus may go through different paths

## Slide 41: Fragmentation (Cont.)
When a datagram is fragmented
  Router must change the values of three fields
    Flags, fragmentation offset, and total length
  Option field may or may not be copied
  The value of checksum must be recalculated regardless of fragmentation

## Slide 42
Figure 8-2
IP Datagram
The McGraw-Hill Companies, Inc., 2000

## Slide 43: Fields Related to Fragmentation
Identification
  16-bit field identifies a datagram originating from the source host
  The combination of the identification and source IP address uniquely define a datagram
  IP uses a counter to label the datagram
  When fragmented, identification field is copied into all fragments
  All fragments have the same identification number

## Slide 44: Fields Related to Fragmentation (Cont.)
Flags: 3-bit field
  1st bit: reserved
  2nd bit: called do not fragment bit
    1: do not fragment.
      If cannot pass through the physical network, router discards the datagram and send an ICMP error message to the source
    0: can be fragmented if necessary
  3rd bit: called the more fragment bit
    1: the datagram is not the last fragment
    0: this is the last or only fragment

## Slide 45
Figure 8-7
Flag Field
The McGraw-Hill Companies, Inc., 2000

## Slide 46: Fields Related to Fragmentation (Cont.)
Fragmentation offset
  The relative position of this fragment with respect to the whole datagram
  Measured in units of 8 bytes
  Thus, the first byte number of each fragment is divisible by 8

## Slide 47
Figure 8-8
Fragmentation Example
The McGraw-Hill Companies, Inc., 2000

## Slide 48
Figure 8-9
Detailed Example
The McGraw-Hill Companies, Inc., 2000

## Slide 49: Reassembly
The first fragment has an offset value of zero
Divide the data length of the first fragment by 8
  The second fragment has an offset value equal to that result
Divide the total length of the first and second fragment by 8
  The third fragment has an offset value equal to that result
Continue the process until the last fragment has a more bit value 0

## Slide 50
Example 7.5
A packet has arrived with an M bit value of 0. Is this the first fragment, the last fragment, or a middle fragment? Do we know if the packet was fragmented?
The McGraw-Hill Companies, Inc., 2000

## Slide 51
If the M bit is 0
  There are no more fragments
  The fragment is the last one
However, we cannot say if the original packet was fragmented or not
A nonfragmented packet is considered the last fragment
Solution

## Slide 52
Example 7.6
A packet has arrived with an M bit value of 1. Is this the first fragment, the last fragment, or a middle fragment? Do we know if the packet was fragmented?
The McGraw-Hill Companies, Inc., 2000

## Slide 53
If the M bit is 1
  There is at least one more fragment
This fragment can be the first one or a middle one, but not the last one
We don’t know if it is the first one or a middle one; we need more information
  The value of the fragmentation offset
However, we can definitely say the original packet has been fragmented because the M bit value is 1
Solution

## Slide 54
Example 7.7
A packet has arrived with an M bit value of 1 and a fragmentation offset value of zero. Is this the first fragment, the last fragment, or a middle fragment?
The McGraw-Hill Companies, Inc., 2000

## Slide 55
The M bit is 1
  Either the first fragment or a middle one.
The offset value is 0
  It is the first fragment
Solution

## Slide 56
Example 7.8
A packet has arrived in which the offset value is 100. What is the number of the first byte? Do we know the number of the last byte?
The McGraw-Hill Companies, Inc., 2000

## Slide 57
To find the number of the first byte
  Multiply the offset value by 8
  The first byte number is 800.
We cannot determine the number of the last byte unless we know the length of the data
Solution

## Slide 58
Example 7.9
A packet has arrived in which the offset value is 100, the value of HLEN is 5 and the value of the total length field is 100. What is the number of the first byte and the last byte?
The McGraw-Hill Companies, Inc., 2000

## Slide 59
The first byte number is 100  8 = 800
The header length is 20 bytes (5  4)
The total length is 100 bytes
  There are 80 bytes in this datagram
If the first byte number is 800, the last byte number must 879
Solution

## Slide 60: Outline
Introduction
Datagram
Fragmentation
Options
Checksum
IP over ATM
Security
IP package

## Slide 61: Options Format
Type field: 1-byte
Length field: 1-byte
  Total length of the option
    Include the type field and the length field
  Not present in all of the option types
Value field: variable-sized
  Contain the data that specific option required
  Not present in all option types
These three fields are often referred to as type-length-value or TLV

## Slide 62
Figure 8-10
Option Format
The McGraw-Hill Companies, Inc., 2000

## Slide 63: Type Field
Copy: 1-bit controls the presence of the option in fragmentation
  0: the option only appear in the first fragment
  1: the option appear in all fragments
Class: 2-bit defines the general purposes of the option
  00: the option is used for datagram control
  10: the option is used for debugging and management
  01 and 11: have not yet been defined
Number: 5-bit defines the type of the option
  only 6 types are in use

## Slide 64: Option Types
Only 6 options are currently being used
Two of them are 1-byte option
  Do not require the length or the value fields
Four of them are multiple-byte option
  Require the length and the value fields

## Slide 65
Figure 8-11
Categories of Options
The McGraw-Hill Companies, Inc., 2000

## Slide 66
Figure 8-2
IP Datagram
The McGraw-Hill Companies, Inc., 2000

## Slide 67: No-Operation Option
Used as a filler between options
For example, used to align the next option on a 16-bit or 32-bit boundary

## Slide 68: End-of-Option Option
Used for padding at the end of the option field
  Can only be used as the last option
  Only one end of option option can be used
  After this option
    The receiver check for the payload data
  Thus, if more than 1 byte is needed to align the option field
    Some no operation options must be used followed by an end of option option

## Slide 69: End-of-Option Option (Cont.)

## Slide 70: Record-Route Option
Used to record the routers that handle the datagram
  Can list up to nine router IP address since the maximum size of option part in an IP header is 40 bytes
Pointer: an offset integer field containing the byte number of the first empty entry
  Point to the first available entry

## Slide 71
Figure 8-14
Record-Route Option
The McGraw-Hill Companies, Inc., 2000

## Slide 72: Record-Route Option (Cont.)
Initially the pointer field has a value of 4
When receiving this datagram, the router
  Insert its outgoing IP address in the empty field
  Increment the value of the pointer by 4

## Slide 73
Figure 8-15
Record-Route Concept
The McGraw-Hill Companies, Inc., 2000

## Slide 74: Strict-Source-Route Option
Used by the source to predetermine a route for the datagram
Rule
  All the routers defined in the option must be visited
  A router must not be visited if its IP address is not listed in the datagram

## Slide 75: Strict-Source-Route Option (Cont.)
If the datagram visits a router not on the list
  Discard the datagram and issue an error message
If the datagram arrives at the destination and some of the entries were not visited
  Discard the datagram and issue an error message

## Slide 76
Figure 8-16
Strict-Source-Route Option
The McGraw-Hill Companies, Inc., 2000

## Slide 77: Strict-Source-Route Operations
When a datagram arriving at a router, compare the pointer value with the length field
  If pointer <= length, compare the IP address pointed by the pointer with its incoming IP address
    If equal,
      Process the packet
      Overwrite the current IP address with its incoming IP address
      Increment the pointer by 4
      Forward the packet
    If not equal, discard the datagram and issue an error message
  If pointer > length, discard the datagram and issue an error message

## Slide 78: Strict-Source-Route Concept

## Slide 79: Loose-Source-Route Option
Each router in the list must be visited
But the datagram can visit other routers as well

## Slide 80: Timestamp
Used to record the time of datagram processing by a router
  Expressed in millisecond from midnight, Universal Time
  Help to track the behavior of the router

## Slide 81
Figure 8-19
Timestamp Option
The McGraw-Hill Companies, Inc., 2000

## Slide 82: Timestamp Option Format
Overflow field
  The number of routers that could not add their timestamp because no more fields were available
Flag: the visited router responsibilities
  0: each router add only timestamp in the provided field
  1: each router add its outgoing IP address and timestamp
  3: the IP address are given. Each router check the given IP address with its own incoming IP address
    If match, overwrite with its outgoing IP address and add timestamp

## Slide 83
Figure 8-20
Use of Flag in Timestamp
The McGraw-Hill Companies, Inc., 2000

## Slide 84
Figure 8-21
Timestamp Concept with Flag Value of 1
The McGraw-Hill Companies, Inc., 2000

## Slide 85
Example 7.10
Which of the six options must be copied to each fragment?
The McGraw-Hill Companies, Inc., 2000

## Slide 86
Look at the first (left-most) bit of the code for each option
  No operation: Code is 00000001; no copy.
  End of option: Code is 00000000; no copy
  Record route: Code is 00000111; no copy
  Strict source route: Code is 10001001; copied
  Loose source route: Code is 10000011; copied
  Timestamp: Code is 01000100; no copy
Solution

## Slide 87
Example 7.11
Which of the six options are used for datagram control and which are used for debugging and management?
The McGraw-Hill Companies, Inc., 2000

## Slide 88
Look at the second and third (left-most) bits of the code
  No operation: Code is 00000001; control
  End of option: Code is 00000000; control
  Record route: Code is 00000111; control
  Strict source route: Code is 10001001; control
  Loose source route: Code is 10000011; control
  Timestamp: Code is 01000100; debugging
Solution

## Slide 89
One of the utilities available in UNIX to check the travelling of the IP packets is ping.
Ping a server named fhda.edu and the result shows that the IP address of the host is 153.18.8.1
Example 7.12

## Slide 90
We can also use the ping utility with the -R option to implement the record route option
Example 7.13

## Slide 91
The traceroute utility can also be used to keep track of the route of a packet
The result shows the three routers visited.
Example 7.14

## Slide 92
The traceroute program can be used to implement loose source routing.
  The -g option allows us to define the routers to be visited, from the source to destination.
  Following shows how we send a packet to the fhda.edu server with the requirement that the packet visit the router 153.18.251.4
Example 7.15

## Slide 93
The traceroute program can also be used to implement strict source routing.
  The -G option forces the packet to visit the routers defined in the command line.
  Following shows how we send a packet to the fhda.edu server and force the packet to visit the router 153.18.251.4
Example 7.16

## Slide 94: Outline
Introduction
Datagram
Fragmentation
Options
Checksum
IP over ATM
Security
IP package

## Slide 95: Checksum
Error detection method
Checksum calculation at the sender
  The packet is divided into k section, each of n bits
  All sections are added together using one’s complement arithmetic
  The final result is complemented to make the checksum

## Slide 96: 補充:Addition in One's Complement
Addition of signed numbers in one's complement is performed using binary addition with end-around carry.
  Add any resulting carry back into the resulting sum

## Slide 97: 補充:Addition in One's Complement (Cont.)
Add decimal 17 to decimal -8 in 8-bit one's complement:

## Slide 98: Checksum (Cont.)
Checksum calculation at the receiver
  Divides the received packet, including the checksum, into k section
  Add all section and then complement the result
  If the final result is 0, the packet is accepted
    Otherwise, reject the packet

## Slide 99
Figure 8-2
IP Datagram
The McGraw-Hill Companies, Inc., 2000

## Slide 100
Figure 8-22
Checksum Concept
The McGraw-Hill Companies, Inc., 2000

## Slide 101: Checksum Concept
According to the one’s complement arithmetic
  If all the section are added and the number is T
  Complement T in one’s complement is –T
  Thus, if the sum is T, the checksum is –T
When the receiver receives the packet
  T + (-T) in one’s complement is -0
  Complement -0 derive 0
  Thus, the final result should be 0

## Slide 102
Figure 8-23
Checksum in One’s Complement Arithmetic
The McGraw-Hill Companies, Inc., 2000

## Slide 103: Example:
T =01110101 (= 117)
-T=10001010 (= -127) = checksum
T+(-T) = 1111 1111 (= -0)
-(T+(-T))= 00000000 (=+0)

## Slide 104: Checksum in the IP Packet
The checksum in the IP packet covers only the header, not the data. This is because
  All higher-level protocols that encapsulate data in the IP datagram have a checksum field
    Checksum for the IP datagram do no have to check the encapsulated data
  The header of the IP datagram changes with each visited router, but the data does not
    If the data is included, each router must recalculate the checksum including data

## Slide 105
Example 7.17: Checksum Calculation in Binary

## Slide 106
Example 7.18: Checksum Checking in Receiver

## Slide 107: Outline
Introduction
Datagram
Fragmentation
Options
Checksum
IP over ATM (Skip!)
Security
IP package (Skip)

## Slide 108: Security
No security was provided for the IPv4 protocol
  The IPv4 was started when the Internet users trusted each other
However, today, the Internet is not secure any more
Security Issues
  Packet Sniffing (嗅,聞) (偷看封包的內容)
  Packet Modification
  IP Spoofing (愚弄)

## Slide 109: Packet Sniffing
An intruder intercepts an IP packet and make a copy of it
A passive attack
  Since not change the contents of the packet
Very difficult to detect
Solution: encryption

## Slide 110: Packet Modification
An intruder modifies the packet
  Intercepts the packet, changes its contents, and sends the new packet to the receiver
Solution: data integrity

## Slide 111: IP Spoofing
An attacker can masquerade(冒充) as somebody else and create an IP packet that carries the source address of another computer
Solutions: origin authentication

## Slide 112: IPSec
The IP packet today can be protected by IPSec (IP Security) protocol
IPSec provides the following four services
  Defining algorithms and keys
  Packet encryption
  Data integrity
  Origin authentication

## Slide 113: Outline
Introduction
Datagram
Fragmentation
Options
Checksum
IP over ATM (Skip!)
Security
IP package (Skip)