## Slide 1: Chapter 9 Internet Control Message Protocol Version 4 (ICMPv4)

## Slide 2: Outline
Introduction
Message
Debugging Tools
ICMP Package

## Slide 3: Introduction
IP provides unreliable and connectionless datagram delivery
Drawbacks
  Lack of error control mechanism
  Lack of assistance mechanism
Solution
  ICMP

## Slide 4: Lack of Error Control Mechanism
No error-reporting or error-correcting mechanism
  What happens if a router must discard a datagram because
    Cannot find a router to the destination
    Time-to-live field has a zero value
  What happens if the final destination host must discard all received fragments of a datagram
    Because it has not received all fragments within a predefined time limit

## Slide 5: Lack of Assistance Mechanism
Lack of a mechanism for host and router for management queries
  How to determine if a router or another host is alive?
  How to obtain information from another host or router?

## Slide 6: Solution
ICMP: Internet Control Message Protocol
  A network layer protocol
  However, its message are not passed directly to the data link layer
  The message are first encapsulated inside IP datagram before going to the lower layer

## Slide 7
Position of ICMP in TCP/IP Protocol Suite
The McGraw-Hill Companies, Inc., 2000

## Slide 8
Figure 9-2
Encapsulation of ICMP Packet
The McGraw-Hill Companies, Inc., 2000

## Slide 9: Outline
Introduction
Message
Debugging Tools
ICMP Package

## Slide 10: ICMP Messages
ICMP messages are divided into
  Error-reporting message
    Report problems that a router or a host (destination) may encounter when it processes an IP packet
  Query message
    Help a router or a network manager to get specific information from a router or another host

## Slide 11: ICMP Messages

## Slide 12
Figure 9-4
General Format of ICMP Messages
The McGraw-Hill Companies, Inc., 2000

## Slide 13: Message Format
8-byte header
  The first 4-byte are common to all
    Type(1-byte): define the type of the message
    Code(1-byte): specify the reason for the particular message type
    Checksum(2-byte)
  The rest is specific for each message type
A variable-size data section
  For error-reporting message
    Carries information for finding the original packet that had the error
  For query message
    Carries extra information based on the type of the query

## Slide 14: Error Reporting Messages
ICMP only report error
  Does not correct error
  Error correction is left to the higher-level protocol
Error reporting message are always sent to the original source

## Slide 15
Figure 9-5
Error-Reporting Messages
The McGraw-Hill Companies, Inc., 2000

## Slide 16: Important Points about ICMP Error Messages
No ICMP error message for a datagram carrying an ICMP error message
  Prevent the problem of infinite loop
No ICMP error message for a fragmented datagram that is not the first fragment
No ICMP error message for a datagram having a multicast address.
No ICMP error message for a datagram with a special address such as 127.0.0.0 or 0.0.0.0.

## Slide 17: ICMP Packet Data Section
The data section in all error message contain includes
  The IP header of the original datagram
    Give the original source information about the datagram itself
  The first 8-byte of data in that datagram
    Provides information about the port number (UDP and TCP) and sequence number (TCP)
    Source then can inform the upper layer protocols (TCP or UDP) about the error

## Slide 18
Figure 9-6
Contents of Data Field for Error Messages
The McGraw-Hill Companies, Inc., 2000

## Slide 19: Destination Unreachable
When a router cannot route a datagram or a host cannot deliver a datagram
  Discard the datagram
  The router or host sends a destination unreachable message back to the source host

## Slide 20: Code Field for Destination-Unreachable
Code 0: the network is unreachable
  Possibly due to hardware failure
  Can only be generated by a router
Code 1: the host is unreachable
  Possibly due to hardware failure
  Can only be generated by a router
Code 2: the protocol is unreachable
  Delivery to the upper layer protocol (TCP, UDP) is failed
  Can only be generated by a destination host

## Slide 21: Code Field for Destination-Unreachable (Cont.)
Code 3: the port is unreachable
  Can only be generated by the destination host
Code 4: fragmentation is required, but the DF (do not fragment) field has been set
  The sender specifies no fragmentation
  But the router is impossible without fragmentation
Code 5: source routing cannot be accomplished
  One or more routers defined in the source routing cannot be visisted

## Slide 22: Code Field for Destination-Unreachable (Cont.)
Code 6: the destination network is unknown
  In code 0: the router knows that the destination network exists, but it is unreachable at the moment
  In code 6: the router has no information about the destination network
Code 7: the destination host is unknown
  In code 1: the router knows that the destination host exists, but it is unreachable at the moment
  In code 7: the router is unaware of the existence of the destination host

## Slide 23: Code Field for Destination-Unreachable (Cont.)
Code 8: the source host is isolated
Code 9: communication with the destination network is administratively prohibited
Code 10: communication with the destination host is administratively prohibited
Code 11: the network is unreachable for the specified type of service
Code 12: the host is unreachable for the specified type of service

## Slide 24: Code Field for Destination-Unreachable (Cont.)
Code 13: the host is unreachable because the administrator has put a filter on it
Code 14: the host is unreachable because the host precedence is violated
  The requested precedence is not permitted for the destination
Code 15: the host is unreachable because its precedence was cut off

## Slide 25
Destination-unreachable messages with codes 2 or 3 can be created only by the
destination host. Other destination-unreachable messages can be created only by routers.
Note

## Slide 26: Error Reporting
Even if a router does not report a destination-unreachable message
  Does not mean that the datagram has been delivered
  For example, in a Ethernet network, there is no way that a router knows a packet has been delivered to the destination or the next router
    Ethernet does not provide an acknowledge mechanism

## Slide 27
A router cannot detect all problems that prevent the delivery of a packet.
Note

## Slide 28: Source Quench
In IP, there is no communication between the source host, the router, and the destination
Thus, no flow control and congestion control in IP
  The source never knows if it is producing datagram faster than can be
    Forwarded by router
    Processed by the destination host
Problem
  Packet losses in routers or the destination host

## Slide 29: Source Quench (Cont.)
Source-quench message thus adds a kind of flow control and congestion control to the IP
  Inform the source that the datagram has been discarded
  Warm the source that
    There is congestion somewhere in the path
    The source should slow down (quench) the sending process

## Slide 30
A source-quench message informs the source that a datagram has been discarded due to congestion in
a router or the destination host.
The source must slow down the sending of datagrams until the congestion is relieved.
Note

## Slide 31: Note about the Source Quench
One source-quench message should be sent for each datagram that is discarded due to congestion
There is no mechanism to tell the source that the congestion has been relieved and the source can speed up its sending rate
  The source continue to slower the rate until no more source-quench message are received

## Slide 32: Note about the Source Quench (Cont.)
The congestion can be created either by one-to-one or many-to-one communication
  In one-to-one: source quench is helpful
  In many-to-one: may be useless
    Each source sends datagram at a different rate
    The router or the destination has no clue which source is responsible for the congestion
    Thus, it may drop a datagram from a very slow source

## Slide 33
One source-quench message is sent for each datagram that is discarded due to congestion.
Note

## Slide 34
Figure 9-5
Error-Reporting Messages
The McGraw-Hill Companies, Inc., 2000

## Slide 35: Time Exceeded: Two Situations
The packet travel in a loop or a cycle
  Caused by errors in the routing table
  Finally, time-to-live value is 0
  The router discards the datagram and sends time-exceeded message
When all fragment that make up a message do not arrive at the destination within a certain time limit
  When the first datagram arrives at the destination, it starts a timer
  When the timer expires and all the fragments are not arrived
  The destination discards all the fragments and sends a time-exceeded message

## Slide 36
Figure 9-9
Time-Exceeded Message Format
Code 0: Time to live is zero
Code 1: Fragmentations are not arrived with a set time
The McGraw-Hill Companies, Inc., 2000

## Slide 37: Parameter Problem
Occurred when a router or a destination discovers an ambiguous or missing value in any field of the datagram
Code 0: there is an error or ambiguity in one of the header fields
  Pointer field points to the byte within the problem
Code 1: the required part of an option is missing

## Slide 38
Figure 9-10
Parameter-Problem Message Format
Code 0: Main header problem Code 1: Problem in the option field
The McGraw-Hill Companies, Inc., 2000

## Slide 39
A parameter-problem message can be created by a router or the destination host.
Note

## Slide 40: Redirection
Routing table is updated dynamically
However, for efficiency, hosts do not take part in the routing update process
  There are terrible number of hosts
  Host thus use static routing
    Usually knows only one IP address of the router, the default router
Thus, the host may send a datagram to the wrong router

## Slide 41
Figure 9-11
Redirection Concept
The McGraw-Hill Companies, Inc., 2000

## Slide 42
A host usually starts with a small routing table that is gradually augmented and updated.
One of the tools to accomplish this is the redirection message.
Note

## Slide 43
Figure 9-12
Redirection Message Format
Code 0: Redirection for a network-specific route Code 1: Redirection for a host-specific route Code 2: Redirection for a network-specific route based on a specified type of service
Code 3: Redirection for a host-specific route based on a specified type of service
The McGraw-Hill Companies, Inc., 2000

## Slide 44
A redirection message is sent from a router to a host on the same local network.
Note

## Slide 45: Query Messages
ICMP can also diagnose some network problems
  Accomplished by the query message
A group of five different pair of messages
  Three of these pairs are deprecated today
  Only two pairs are used today
    Echo request and reply
    Timestamp request and reply

## Slide 46: ICMP Messages

## Slide 47: Echo Request and Reply
Determine whether two systems (hosts or routers) can communicate with each other
  Determine if there is communication at the IP level
    Because ICMP are encapsulated in IP datagrams
  Also be used by a host to see if another host is reachable
    At the user level, this is done by ping command

## Slide 48
Figure 9-14
Echo-Request and Echo-Reply
Message Format
The McGraw-Hill Companies, Inc., 2000
Identifier and sequence number
  Are not formally defined by the protocol
  Can be used arbitrarily by the sender

## Slide 49: Timestamp Request and Reply
Two goals
  Determine the round-trip time needed for an IP datagram
  Synchronize the clocks in two machines

## Slide 50: Timestamp
Original timestamp
  Filled by the sender at departure time
  Appear in both request and reply messages
Receive timestamp
  Filled by the receiver at receiving time
  Appear only at the reply message and fill zero in request message
Transmit timestamp
  Filled by the receiver when the reply message departs
  Appear only at the reply message and fill zero in request message

## Slide 51: One-Way and Round-Trip Time
Sending time = value of receive timestamp -
value of original timestamp
Receiving time = time the packet returned -
value of transmit timestamp
Round-trip time = sending time +
receiving time

## Slide 52: One-Way and Round-Trip Time (Cont.)
Note that
  Sending time and receiving time are accurate only if the clocks in the source and destination are synchronized
  The round-trip time is correct even if the two clocks are not synchronized
    See the following next slides

## Slide 53: Example
Given
  Value of original timestamp: 46
  Value of receive timestamp: 59
  Value of transmit timestamp: 60
  Time the packet arrived: 67
Derive
  Sending time = 59 - 46 = 13 milliseconds
  Receiving time = 67 - 60 = 7 milliseconds
  Round-trip time = 13 + 7 = 20 milliseconds

## Slide 54: Example (Cont.)
To show that the round-trip time is independent of time difference
  Following above example, assume that the time difference is 3
    Receiving node’s clock = 3 + sending node’s clock
  Sending time = (56+3) – 46 = 10 + 3
  Receiving time = 67 – (57+3) = 10 – 3
  RRT = (10 + 3) + (10-3) = 20

## Slide 55: Synchronization
Timestamp request and timestamp reply messages can also by used to synchronize the clocks in two machines

## Slide 56: Example (Cont.)
Time difference = receive timestamp -
(original timestamp field + one-way time duration)
Assume the one-way time duration can be obtained by dividing the round-trip time duration by two
  Note that, this assumption may be wrong, depends on the network condition
Thus, time difference = 59 - (46 + 10) = 3

## Slide 57: Deprecated Messages
Three pairs of messages are declared obsolete by IETF
  Information request and reply messages
    Their duties are done by ARP
  Address mask request and reply message
    Their duties are done by DHCP (Dynamic Host Configuration Protocol)
  Router solicitation and advertisement message
    Their duties are done by DHCP

## Slide 58: Checksum
In ICMP, the checksum is calculated over the entire message
Checksum calculation
  The checksum field is set to zero
  The sum of all the 16-bit words (header and data) is calculated
  The sum is complemented to get the checksum
  The checksum is stored in the checksum field

## Slide 59: Checksum (Cont.)
Checksum testing
  The sum of all words (header and data) is calculated
  The sum is complemented
  If the result is 16 0s, the message is accepted
    Otherwise, it is rejected

## Slide 60
The McGraw-Hill Companies, Inc., 2000
Example 9.1: Checksum Calculation

## Slide 61: Outline
Introduction
Message
Debugging Tools
ICMP Package

## Slide 62: Ping
To find if a host is alive and responding
Operations
  Source sends ICMP echo request message (type: 8, code:0)
    Start the sequence number from 0 and increments each time a new message is sent
  Destination responds with ICMP echo reply message
  Can calculate the round trip time
    Insert the sending time in the data section
    When the packet arrives, subtract the arrival time from the departure time to get the RTT

## Slide 63
Example 9.2

## Slide 64
From above example
  Sequence number starts from 0
  TTL (Time to live) = 62
  At the beginning
    Data bytes is 56 bytes
    Total number of bytes is 84 (= 56 + 8 + 20)
      8 = ICMP header, 20 = IP header
    The total number of bytes in the ICMP packet is 64 (= 56+8)
Example 9.2 (Cont.)

## Slide 65: Traceroute
Trace the route of a packet from the source to the destination
  TRACERT in windows
An application program that uses the services of UDP
Elegantly use two ICMP message
  Time exceeded
  Destination unreachable

## Slide 66: Traceroute Operation
In the following figure
  the traceroute program uses the following steps to find the address of R1 and RTT between host A and R1
    Traceroute at host A sends a UDP packet to B and set IP’s TTL field = 1
    R1 receives the packet and decrements the value of TTL to 0.
      Discard the packet and sends a time-exceeded ICMP message since the TTL value is 0
    The traceroute at host A receives the ICMP message and find the source address of the IP packet = IP address of R1
    Repeat the a~c steps three times to get a better average RTT value
      Since the first RTT would by much longer since ARP operation
  Traceroute program repeats the previous steps with TTL = 2 to find the address of R2 and RTT between host A and R2

## Slide 67: The Traceroute Program Operation

## Slide 68: Traceroute Operation (Cont.)
  Repeats the previous steps to find the address of host B and the RTT between host A and B
    When host B receives the UDP packet
      Decrement TTL to 0
      Receive the packet since it is the destination (do not discard)
    How can an ICMP message be sent back to host A?
      The destination port of UDP packet is sent to one that is not supported by the UDP protocol
      Host B cannot delivery the packet to an application
      Thus, host B discard the UDP packet and sends an ICMP destination-unreachable message to host A
    Once host A receiving a destination-unreachable message with code value 3
      The whole route has been found

## Slide 69
The un-numbered line shows that
  The destination is 153.18.8.1.
  The TTL value is 30 hops.
  The packet contains 38 bytes: 20 bytes of IP header, 8 bytes of UDP header, and 10 bytes of application data.
    The application data is used by traceroute to keep track of the packets
The first line shows the first router visited.
  The router is named Dcore.fhda.edu with IP address 153.18.31.254.
  The first round trip time was 0.995 milliseconds, the second was 0.899 milliseconds, and the third was 0.878 milliseconds
$ traceroute fhda.edu traceroute to fhda.edu (153.18.8.1), 30 hops max, 38 byte packets 1 Dcore.fhda.edu (153.18.31.254) 0.995 ms 0.899 ms 0.878 ms 2 Dbackup.fhda.edu (153.18.251.4) 1.039 ms 1.064 ms 1.083 ms 3 tiptoe.fhda.edu (153.18.8.1) 1.797 ms 1.642 ms 1.757 ms
Example 9.4

## Slide 70
An interesting point is that a host can send a traceroute packet to itself.
This can be done by specifying the host as the destination.
The packet goes to the loopback address as we expect
$ traceroute voyager.deanza.edu traceroute to voyager.deanza.edu (127.0.0.1), 30 hops max, 38 byte packets 1 voyager (127.0.0.1) 0.178 ms 0.086 ms 0.055 ms
Example 9.6

## Slide 71: Outline
Introduction
Message
Debugging Tools
ICMP Package (Skip!)

## Slide 72: 範圍：CHAPTER 6~9 日期：12/9
第二次考試